## Slide 1: Fall Prevention in Residential Construction
Fall hazard awareness, prevention, solutions, and rescue.

## Slide 2: Welcome!
This training is provided as a service to the residential construction industry by:
jssafety.org nahb.org/safety
Notes: Provide an overview of JSI and NAHB.
Job-Site Safety Institute (JSI) is a nonprofit organization dedicated to conducting safety research for residential and commercial job-sites. JSI serves as a research center where educational institutions and industry leaders collaborate and exchange ideas to increase awareness of the inherent dangers of a construction site.
The National Association of Home Builders (NAHB) helps its members build communities. Since it was founded in the early 1940s, NAHB has served as the voice of America’s housing industry. We work to ensure that housing is a national priority and that all Americans have access to safe, decent and affordable housing, whether they choose to buy a home or rent.

## Slide 3: Disclaimer
This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.
This presentation is intended to discuss Federal Regulations only - your individual State requirements may be more stringent as many states operate their own state OSHA and they may have adopted construction standards that are different from information presented in this training. If you live in a state with an OSHA approved state plan, you should contact your local administrator for further information on the standards applicable in your state.
These materials are meant for informational purposes only.
No representation is made as to the thoroughness of the presentation.
Notes: This material was produced under the Susan Harwood training grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 4: Disclaimer, continued 1
It is not the intent to provide compliance-based training in this presentation, the intent is more to address hazard awareness in the residential construction (i.e. home building) industry, and to recognize the overlapping hazards present in many construction workplaces.
Photos shown in this presentation may depict situations that are not in compliance with applicable OSHA/safety requirements.
No legal advice is offered or implied, and no attorney-client relationship is intended or established. If legal advice or other expert assistance is required the services of a competent professional person should be sought.
It is the responsibility of the employer and its employees to comply with all pertinent OSHA/safety rules and regulations in the jurisdiction in which they work.
Notes: Please read the disclaimer for legal purposes, this is required under the Susan Harwood Training Grant program.

## Slide 5: Copyright Information © 2018
This material is the copyrighted property of the Job-Site Safety Institute and the National Association of Home Builders. By federal regulation, OSHA reserves a license to use and disseminate such material for the purpose of promoting safety and health in the workplace. The Job-Site Safety Institute and the National Association of Home Builders hereby authorizes employers and workplace safety and health professionals to use this material, distributed by or through OSHA, in their workplaces or practices in accordance with the guidance contained in the material.
To this end, permission is granted to use such copyrighted material solely for non-commercial, instructional, personal, or scholarly purposes. The material may be used and incorporated into other workplace safety and health programs on the condition that no fee may be charged for the subsequent use of the material. Use of the material for any other purpose, particularly commercial use, without the prior, express written permission of the copyright owner/s is prohibited. Furthermore, any modification to the material is prohibited without the prior, express written permission of the copyright owners.
Notes: Note that the these materials are copyrighted by the Job-Site Safety Institute and the National Association of Home Builders. Permission is granted to use such copyrighted material in accordance with the terms on the slide.

## Slide 6: Course Agenda
Section 1: Introduction / Overview of Fall Protection - 30 minutes
Section 2: Ladders - 30 minutes
Section 3: Scaffolds - 45 minutes
Section 4: Conventional Fall Protection - 60 minutes
Section 5: Additional Fall Protection Systems - 60 minutes
Section 6: Rescue - 15 minutes

## Slide 7: Course Objectives
Recognize common fall hazards in residential construction.
Identify when fall protection is required.
Determine which protection system to use for a given fall hazard.
Understand the key requirements and basic safety practices for each protection system.
Understand the safety requirements and practices for ladders and scaffolding.

## Slide 8: Section 1
Overview of fall protection

## Slide 9: Learning Objectives: Section 1
State why fall protection is important.
Identify common fall hazards in residential construction.
Define “residential construction”.
Understand the importance of fall protection training.
Understand competent and qualified persons requirements.
Notes: Discuss the learning objectives for Section 1. Elaborate on the 5 key learning objectives. Allow time for attendees to read and understand what will be taught during the first section and take time to answer any questions.

## Slide 10: Fall Protection – Unsafe Photos
Notes: Briefly discuss the fall hazards present in the picture shown. We will discuss these hazards in greater detail throughout the course of this presentation.

## Slide 11: Introduction To Fall Protection
The goals of this course are to help you:
  Understand how to identify, correct or eliminate fall hazards on your job sites.
  Understand the regulatory requirements to protect and train workers to prevent falls on home building job sites.
  Gain a more thorough understanding of OSHA regulations applicable to home building.
Notes: Discuss the goals of the course, including:
Understand how to identify, correct or eliminate fall hazards on your job sites.
Understand the regulatory requirements to protect and train workers to prevent falls on home building job sites.
Gain a more thorough understanding of OSHA regulations applicable to home building.

## Slide 12: Introduction To Fall Protection, continued 1
Participants can use the information from this seminar to:
  Provide training to employees.
  Develop fall protection best practices for employees to use on the jobsite.
  Understand the types of conventional fall protection systems that can be used on home building jobsites.
Notes: Discuss the many benefits that participants of this class can expect to receive. They include but are not limited to:
Providing training to employees
Developing fall protection best practices
Implementing a fall protection plan, as needed, in accordance with 1926.502(k)

## Slide 13: Why Is Fall Protection Important?
Falls are the leading cause of serious and fatal injuries in residential construction.
Between 2003 and 2010: 1,917 workers died in the U.S. residential construction industry.
  Nearly half (45.3%) of the fatalities were from falls.
  In the residential roofing industry, 80.2% of fatalities were from falls.
  Falls from ladders accounted for 23.0% of fatal falls in residential construction.
Notes: Discuss the importance of taking proactive steps to protect workers from fall hazards in the residential construction industry.
Emphasize that falls are the leading cause of fatalities in the construction industry to really open participants eyes about the severity of this hazard and the injuries associated with it.
Source: https://www.cpwr.com/sites/default/files/publications/DongFatalFallsInResidentialConstructionKF.pdf (Bureau of Labor Statistics’ Census of Fatal Occupational Injuries)

## Slide 14: How far is too far to fall?
More than 40% of fatal falls occurred from heights 15 feet or lower.
  15 feet is only 5-yards on a football field.
  15 feet is only 1.5 times the height of a basketball rim.
Notes: Explain that serious injuries and fatalities can occur when falling from heights of less than 15 feet. Compare the height of a basketball hoop to the height of 15 feet, or the length of 5-yards on a football field.

## Slide 15: Percent of fatal falls to a lower lever by height of fall, 2015
Source: U.S. Department of Labor, Bureau of Labor Statistics
Notes: In 2015, the total for falls to lower level was 648 fatal work injuries. Of the cases where height of fall was known (538 cases), more than 2 out of every 5 fatal falls were falls of 15 feet or less. About one in five cases with a known height involved falls from more than 30 feet.

## Slide 16: Top 10 OSHA Citations FY2017
Top 10 OSHA Citations in Construction
1. Fall Protection – duty to have fall protection.
2. Scaffolding – general requirements.
3. Ladders
4. Fall Protection – training requirements.
5. Personal Protective Equipment – eye and face protection.
6. Personal Protective Equipment – head protection.
7. Hazard Communication – toxic and hazardous substances.
8. Scaffolds – aerial lifts.
9. General Safety & Health Provisions
10. Fall Protection – fall protection systems, criteria.
Notes: Discuss the top 10 OSHA Citations in Construction for FY2017. Emphasize that 5 of the top 10 most frequently cited standards are related to fall protection.

## Slide 17: FY2017 OSHA Top 10 by the Numbers
32,000 citations were issued by OSHA in its top 10 most frequently cited categories.
$2,600,000 ($2.6M) – largest citation issued by OSHA after a single visit to one employer.
6,887 violations issued for OSHA’s #1 most frequently cited standard – fall protection.
  4,252 citations were related to failing to provide conventional fall protection.
Notes: Emphasize that OSHA has the authority to issue substantial monetary citations against companies who fail to comply with their regulations. For example, in FY2017 OSHA issued a $2.6 Million fine to an employer after a single visit to their jobsite.

## Slide 18: Did you hear about OSHA Fines Going
In 2016, OSHA increased fines by 78%.
OSHA last raised fines in 1990.
Notes: Discuss that in 2016 OSHA increased fines by 78%. The new maximum penalties for serious, fail to abate, and willful or repeated violations are shown in the slide.

## Slide 19: Fall Protection – Unsafe Photos, continued 1
Notes: Photo depicts workers along the leading edge of a building without conventional fall protection. Use this as a talking point to see if attendees think this is acceptable or not.

## Slide 20: Fall Protection – Unsafe Photos, continued 2
Notes: Image shows a worker not tied off to an approved anchor point. Use this as a discussion to see if attendees can identify the hazards.

## Slide 21: What does OSHA require for fall protection?
Workers exposed to a fall hazard 6 ft. (1.8 m) or more above lower levels must be protected by conventional fall protection (i.e., guardrail systems, safety net systems or PFAS).
Notes: OSHA requires the use of conventional fall protection if workers are exposed to fall hazards 6 ft. or more above a lower level when performing construction.

## Slide 22: Overview of Regulations
6 feet is the trigger height for when fall protection is required for construction sites.
Notes: 6 feet is the trigger height at when fall protection is required on construction sites.

## Slide 23: Overview of Regulations, continued 1
There is a 10 foot trigger height when working on scaffolding.
Notes: 10 feet is the trigger height at when fall protection is required when working off a scaffold.

## Slide 24: Overview of Regulations, continued 2
There is no trigger height for fall protection systems when working on ladders.
Notes: There is no trigger height for when fall protection is required when working off a ladder.

## Slide 25: Requirements on Jobsites
Some OSHA State-Plan states may have different trigger heights of when conventional fall protection is required on residential jobsites.
These states include, but may not be limited to:
  California
  Kentucky
  North Carolina
  Arizona
  Washington
  Oregon
Notes: Discuss how some states may have different trigger heights for when conventional fall protection is required on residential jobsites.

## Slide 26: Where Do You Start?
Understand OSHA Fall Protection Regulations.
Evaluate fall hazards and implement conventional fall protection systems.
Train workers to identify hazards.
Appoint a competent person responsible for fall protection on the jobsite.
Develop a written fall protection plan, as needed, in accordance with §1926.502(k).
Notes: Discuss the initial steps that must be taken to comply with OSHA fall protection regulations, and protect workers on a residential construction jobsite.
Fall protection plans, as needed, in accordance with OSHA’s §1926.502(B)(13) regulation will be discussed in Section 6 of the training presentation.

## Slide 27: Fatal Accidents
Accident #1
A worker was walking along a one-story pitched roof on a residential structure as he was installing flashing around PVC pipe roof vents. He was near the peak of the roof, when he fell through a fireplace chimney opening.
The worker fell at least 20 ft. (6.1 m) to the fireplace pit area and was killed.
The roof hole had been covered with approximately 1½ inch (3.8 cm) flat Styrofoam sheeting.
What are the fall hazards?
Notes: Discuss this first accident scenario thoroughly. Ask the audience if they have had experience with these hazards, and discuss protective measures that could have been taken to prevent this fatality from occurring.
Encourage audience participation and discussion.

## Slide 28: Fatal Accidents, continued 1
Accident #2
A drywall finisher was sanding the ceiling in a second floor hallway.
He was standing on an open-sided floor above the concrete first floor, when he slipped off the edge and fell 10 ft. (3 m) to the first floor and sustained fatal injuries.
Guardrails had been in place previously but had been removed to move supplies such as doors, drywall, and windows to the second floor.
What are the fall hazards?
Notes: Discuss the second accident scenario thoroughly. Ask the audience if they have had experience with these hazards, and discuss protective measures that could have been taken to prevent this fatality from occurring.
Encourage audience participation and discussion.

## Slide 29: Fatal Accidents, continued 2
Accident #3
A carpenter was on site to perform gutter work on a house.
The worker was climbing an extension ladder that was set up on stone pavers to access the roof.
While climbing the ladder, the victim fell to the ground below when the base of the ladder slipped out and then the ladder fell to the left.
What are the fall hazards?
Notes: Discuss the second accident scenario thoroughly. Ask the audience if they have had experience with these hazards, and discuss protective measures that could have been taken to prevent this fatality from occurring.
Encourage audience participation and discussion.

## Slide 30: What is “Residential Construction”?
Residential construction is defined as construction activity that combines these two elements:
  Residence Requirement: the end-use of the building must be a home or dwelling.
  Wood Frame Construction Requirement: building must be constructed using traditional wood frame construction materials and methods. This includes limited use of structural steel in a predominantly wood framed home, such as a steel I-beam to support wood framing.
Notes: Define residential construction, discuss what is included and excluded and provide examples.

## Slide 31: Is This “Residential Construction”?
Notes: Discuss the picture of a large single-family house and why this is considered residential construction.
This picture shows slide guards installed on the steep-pitch roof; OSHA’s new compliance directive has not outlawed the use of slide guards or safety monitors.
  Now, employers must first demonstrate that it is infeasible to comply with the provisions of the standard, or that it creates a greater hazard.
  Then they can use those systems as part of a written, site-specific fall protection plan that meets the requirements of 1926.502(k).
Slide guards cannot simply be used in lieu of conventional fall protection methods under 1926.501(b)(13). However, slide guards may be used as part of a written, site-specific fall protection plan that meets the requirements of 1926.502(k) if the employer can demonstrate that the use of conventional fall protection (i.e., guardrail, safety net, or personal fall arrest systems) would be infeasible or create greater hazards.
Encourage discussion and participation from the audience.
Refer to the definition of residential construction for further clarification.

## Slide 32: Is This “Residential Construction”?, continued 1
Notes: Discuss that this can be either a residential home, or a small commercial building. Note that just because it has steel framing does not automatically exclude this from the definition of residential construction.

## Slide 33: Is This “Residential Construction”?, continued 2
Notes: Discuss this picture of a multi-family housing complex. Note the differences in construction methods from a typical single-family home, i.e. large worker crane, concrete forms, etc.
Engage the audience and facilitate a short discussion about the picture above.

## Slide 34: Is This “Residential Construction”?, continued 3
Notes: Yes, OSHA considers block wall home construction “residential construction”. OSHA STD 03-11-002 states the agency “has decided that it is consistent with the original purpose of 1926.501(b)(13) to treat the construction of residences with masonry brick or block in the exterior walls as residential construction.”

## Slide 35: Evaluate Fall Protection Systems
Competent person must evaluate the appropriate protective systems, this involves:
  Choose the appropriate system for each unique hazard and situation
  Ensure employees are properly trained on fall protection systems chosen
  Understand manufacturer’s recommendations and limitations of fall protection systems
Notes: Discuss the important role the competent person plays in determining and evaluating the appropriate fall protective system for each fall-related hazard on the jobsite.

## Slide 36: What is a Competent Person?
Through training, someone may be designated as a “Competent Person” for safety-related concerns on a jobsite, including fall hazards/fall protection.
The Competent Person is responsible for:
  Choosing the best system for each unique hazard/situation.
  Ensuring employees are properly trained on the fall protection systems being utilized.
  Understanding the recommendations and limitations of the fall protection systems utilized.
Notes: Discuss that a Competent Person is responsible for understanding appropriate types of fall protection, choosing the right fall protection system for each hazard and ensuring workers are trained.

## Slide 37: Competent Person
On a jobsite, the Competent Person is also responsible for:
  Identifying existing and predictable fall hazards.
  The authority to stop work and eliminate those hazards.
  Authority to take prompt corrective actions.
Notes: Discuss that the competent person is also responsible for the identification of existing and predictable hazards, has the authority to stop work and take prompt corrective actions.

## Slide 38: Fall Protection Training
Employers must train employees to:
Understand the correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems.
The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other methods of fall protection to be used.
Notes: Note: Remember that you must evaluate the use of conventional fall protection systems prior to implementing alternative fall protection systems (i.e. warning lines, safety monitors, controlled access zones).
Discuss the many training requirements when workers are exposed, or have the potential to be exposed to fall hazards on a residential construction jobsite.
1926.501(b)(10)
"Roofing work on Low-slope roofs." Except as otherwise provided in paragraph (b) of this section, each employee engaged in roofing activities on low-slope roofs, with unprotected sides and edges 6 feet (1.8 m) or more above lower levels shall be protected from falling by guardrail systems, safety net systems, personal fall arrest systems, or a combination of warning line system and guardrail system, warning line system and safety net system, or warning line system and personal fall arrest system, or warning line system and safety monitoring system. Or, on roofs 50-feet (15.25 m) or less in width (see Appendix A to subpart M of this part), the use of a safety monitoring system alone [i.e. without the warning line system] is permitted.
Subpart M 29 CFR 1926.503 lists the training requirements for employees exposed to fall hazards.
State that the training must
Facilitate a short discussion from the audience about some of the training they conduct, successful methods of training, the length of the training, and the content.

## Slide 39: Fall Protection Training, continued 1
Employers must train employees on:
Proper use of fall protection equipment.
  Example: always inspect harness before each use and use approved anchor points.
Notes: Photo: http://www.elcosh.org/record/document/1991/32.jpg
Discuss the many training requirements when workers are exposed, or have the potential to be exposed to fall hazards on a residential construction jobsite.
Subpart M 29 CFR 1926.503 lists the training requirements for employees exposed to fall hazards.
State that the training must
Facilitate a short discussion from the audience about some of the training they conduct, successful methods of training, the length of the training, and the content.

## Slide 40: Fall Protection Training, continued 2
Employers must train employees on:
The nature of fall hazards in the work area.
Correct procedures for erecting, maintaining, disassembling and inspecting the fall protection systems to be used.
The use and operation of conventional fall protection systems.
The role of each employee in the fall protection system used.
Notes: Discuss the many training requirements when workers are exposed, or have the potential to be exposed to fall hazards on a residential construction jobsite.
Subpart M 29 CFR 1926.503 lists the training requirements for employees exposed to fall hazards.
State that the training must
Facilitate a short discussion from the audience about some of the training they conduct, successful methods of training, the length of the training, and the content.

## Slide 41: Fall Protection Training, continued 3
Employers must train employees on:
The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs.
The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection.
The role of employees in fall protection plans.
Notes: Discuss the many training requirements when workers are exposed, or have the potential to be exposed to fall hazards on a residential construction jobsite.
Note: Remember that you must evaluate the use of conventional fall protection systems prior to implementing alternative fall protection systems (i.e. warning lines, safety monitors, controlled access zones).
Subpart M 29 CFR 1926.503 lists the training requirements for employees exposed to fall hazards.
State that the training must
Facilitate a short discussion from the audience about some of the training they conduct, successful methods of training, the length of the training, and the content.

## Slide 42: Fall Protection Training, continued 4
Employers must certify training:
Written certification must include:
  Name of employee trained
  Date of training
  Signature of person conducting training
Latest training certification must be maintained
Retrain employees when employer has reason to believe it is necessary or changes have been made to fall protection.
Notes: Discuss the many training requirements when workers are exposed, or have the potential to be exposed to fall hazards on a residential construction jobsite.
Subpart M 29 CFR 1926.503 lists the training requirements for employees exposed to fall hazards.
State that the training must
Facilitate a short discussion from the audience about some of the training they conduct, successful methods of training, the length of the training, and the content.

## Slide 43: Competent Person Responsibilities
Designated competent person:
Responsible for identifying existing and predictable hazards
Has authority to eliminate fall hazards
Has authority to stop work if unsafe conditions exists
Has authorization to take prompt corrective actions to eliminate them
Notes: Discuss the definition of a competent person, their varied roles and responsibilities on a jobsite.
Optional discussion, ask the audience if they have ever served, or are a competent person, and what they have done in their role to fix any fall hazards that may have been present.

## Slide 44: Qualified Person
A qualified person:
  Has a recognizable degree, experience, professional standing, or through extensive knowledge, training and experience has demonstrated the ability to resolve subject matter issues.
  Responsible for design, installation, use and supervision of anchorage points as part of a complete personal fall arrest system.
Notes: Define a qualified person, and some of the roles they are required to perform on a residential construction site, i.e. preparing a fall protection plan.
Anchorages shall be designed, installed and used under the supervision of a qualified person, as part of a complete personal fall arrest system that maintains a safety factor of at least two. Source: Subpart M- Fall Protection

## Slide 45: Section 2
Ladders

## Slide 46: Disclaimer
This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.
This presentation is intended to discuss Federal Regulations only - your individual State requirements may be more stringent as many states operate their own state OSHA and they may have adopted construction standards that are different from information presented in this training. If you live in a state with an OSHA approved state plan, you should contact your local administrator for further information on the standards applicable in your state.
These materials are meant for informational purposes only.
No representation is made as to the thoroughness of the presentation.
Notes: This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 47: Disclaimer, continued 1
It is not the intent to provide compliance-based training in this presentation, the intent is more to address hazard awareness in the residential construction (i.e. home building) industry, and to recognize the overlapping hazards present in many construction workplaces.
Photos shown in this presentation may depict situations that are not in compliance with applicable OSHA/safety requirements.
No legal advice is offered or implied, and no attorney-client relationship is intended or established. If legal advice or other expert assistance is required the services of a competent professional person should be sought.
It is the responsibility of the employer and its employees to comply with all pertinent OSHA/safety rules and regulations in the jurisdiction in which they work.
Notes: Please read the disclaimer for legal purposes, this is required under the Susan Harwood Training Grant program.

## Slide 48: Copyright Information © 2018
This material is the copyrighted property of the Job-Site Safety Institute and the National Association of Home Builders. By federal regulation, OSHA reserves a license to use and disseminate such material for the purpose of promoting safety and health in the workplace. The Job-Site Safety Institute and the National Association of Home Builders hereby authorizes employers and workplace safety and health professionals to use this material, distributed by or through OSHA, in their workplaces or practices in accordance with the guidance contained in the material.
To this end, permission is granted to use such copyrighted material solely for non-commercial, instructional, personal, or scholarly purposes. The material may be used and incorporated into other workplace safety and health programs on the condition that no fee may be charged for the subsequent use of the material. Use of the material for any other purpose, particularly commercial use, without the prior, express written permission of the copyright owner/s is prohibited. Furthermore, any modification to the material is prohibited without the prior, express written permission of the copyright owners.
Notes: Note that the these materials are copyrighted by the Job-Site Safety Institute and the National Association of Home Builders. Permission is granted to use such copyrighted material in accordance with the terms on the slide.

## Slide 49: Learning Objectives: Section 2
Determine the proper ladder to use based on weight capacity and height.
Calculate the proper pitch of extension ladders for proper set-up, and identify how to secure and stabilize ladders.
Identify how to maintain a safe position when using a ladder.
Notes: Discuss the learning objectives for Section 2. In this section we will address ladder and scaffold safety, including:
Determine the proper ladder to use based on weight capacity and height.
Calculate the proper pitch of extension ladders for proper set-up, and identify how to secure and stabilize ladders.
Identify how to maintain a safe position when using a ladder.

## Slide 50: Ladders

## Slide 51: Ladder Hazards
The likelihood of surviving a fall from a ladder at least 10 feet high is only 50%.
Approximately half of all injuries caused by slips, trips or falls from ladders and stairways require time off work.
Notes: Your chances of surviving a fall from a ladder at least 10 feet high is only 50%. Additionally, approximately half of all injuries caused by falls from ladders require time away from work to heal. This can lead to reduced income for your family, and also unnecessary pain and suffering.
Photo from the Electronic Library of Construction Occupational Safety & Health (ELCOSH) http://www.elcosh.org/image/625/i000230/230.html

## Slide 52: Ladder Training Requirements
Each employee using ladders should be trained to recognize hazards.
Hazards Include:
  Nature of the fall hazards in the work area.
  Correct procedures for placement, use and maintenance.
  Maximum intended load-carrying capacities.
Notes: Discuss the training requirements when using ladders. Additionally, employees need to understand the nature of fall hazards, correct procedures for placing and using ladders and the maximum intended load-carrying capacities of ladders so you do not exceed their maximum working load rating.

## Slide 53: Ladder or Scaffold?
Notes: Discuss the unsafe work practice that is utilized here. Rather than use a stepladder, trestle scaffold or other approved equipment, the worker is placing himself in harm’s way by standing on three stacked 5-gallon paint buckets. It is important to always use the right tool for the job.

## Slide 54: Choosing the Right Ladder
Before stepping onto a ladder, think about these things:
What capacity can it hold?
Height of the ladder—too short or too tall?
Condition of the ladder and instructions unique to the ladder selected.
We’ll look at each of these in detail.
Notes: Explain how to pick the right ladder for the task being performed. Remember to pay close attention to the task(s) being performed. Try to think about what capacity the ladder can hold, the height of the area you need to access, and always remember to perform a visual inspection of the ladder prior to use.

## Slide 55: Proper Duty Rating/Capacity
OSHA Requirement
Ladders shall not be loaded beyond the maximum intended load for which they were built nor beyond their manufacturer's rated capacity.
Notes: Discuss the proper duty rating capacity of ladders. Ladders must not be loaded beyond the manufacturers maximum intended load for which they were built to handle.

## Slide 56: Proper Duty Rating/Capacity, continued 1
How much weight will be on the ladder?
  Factor your weight plus tools and materials being handled.
  NOTE: workers must not carry any tools/materials when climbing a ladder that could cause them to lose balance and fall.
Duty rating is the maximum safe load capacity of the ladder.
Notes: Discuss the proper duty rating capacity of ladders. When calculating the duty rating or ladder you need, remember to factor in your weight plus the weight of tools and materials being carried. The duty rating is the maximum safe load capacity of the ladder.
Photo Source: https://www.wernerco.com/us/support/ladder-safety-tips/how-to-choose-a-ladder

## Slide 57: Proper Duty Rating/Capacity, continued 2
Select a ladder with the proper duty rating for your weight and the materials you are handling.
Notes: Explain the table showing duty ratings for a variety of ladder types. For example, a type III light-duty ladder is meant for household use and its maximum intended load rating is 200 lbs. On the opposite spectrum, a type IAA ladder is meant for special heavy duty rugged use and its maximum intended load rating is 375 lbs.

## Slide 58: “3 Feet Rule” for Extension Ladders
When using an extension ladder for access to another level, the ladder must extend at least 3 feet (.9 m) above the landing to provide a hand hold for getting on and off the ladder.
Notes: Emphasize this important rule, requiring the ladder to expend at least 3 feet above the landing or area being accessed. The reason for this requirement is to provide a hand hold for employees to be able to safely get on and off the ladder.

## Slide 59: “3 Feet Rule” for Extension Ladders, continued 1
Add-on extensions to ladders which allow workers to walk-through the top of an extension ladder are acceptable if they extend at least 3 feet (.9 m) above the landing.
Notes: Recognizing that it is important to provide a safe hand hold for workers to get on and off of a ladder, many manufacturers are beginning to make walk-through extensions to avoid having to navigate around the rungs of a ladder. An example of this type of walk-through ladder extension is shown in the slide.
Photo: https://www.osha.gov/pls/oshaweb/owadisp.show_document?p_table=INTERPRETATIONS&p_id=25177

## Slide 60: “3 Feet Rule” for Extension Ladders, continued 2
3 feet
Notes: This picture helps illustrate that a ladder must extend 3 feet beyond the level being accessed. A general rule is that a ladder must extend 3-rungs above the level being accessed as most rungs are placed approximately 12 inches apart.

## Slide 61: Calculate length of Ladder Needed
Extension ladders should be 7 to 10 feet longer than the highest contact point.
  Allows for proper positioning angle and extension above the roof line or landing
Notes: Explain that extension ladders should be at least 7 to 10 feet longer than the height being accessed. This allows for the proper angle for the ladder to be placed, in addition to adding the 3 feet extension above the level being accessed. The chart on the right helps explain this further by providing examples of the height being accessed and also the corresponding ladder height needed.

## Slide 62: Proper Height Stepladders
Choose a stepladder that is no more than 4 feet shorter than the height being reached.
Notes: A stepladder must be no more than 4 feet shorter than the area being reached. This prevents employees from needed to stand on the top 2-rungs of a stepladder, which is unsafe and against OSHA regulations.

## Slide 63: Inspect your Ladder
Inspect ladders prior to use for visible defects.
  Never use a ladder that is broken or otherwise damaged.
  Remove damaged ladders from service, tag them as damaged, and discard them immediately, if feasible.
Notes: Ladders must be inspected at least daily for visible defects. Employees must never use a ladder that is broken or otherwise damaged. Damaged ladders must be removed from service and tagged as defective. An example of a tag to mark a ladder as unsafe and to not use is shown on this slide.

## Slide 64: Inspection of Ladders
Rot, decay of wooden ladders.
Cracked, split, worn or broken rails, braces, steps.
Missing identification or safety labels.
Do not paint ladders since defects may be concealed.
Missing, broken or loose rungs.
Damaged or worn non-slip feet.
Loose nails, screws, bolts, rivets.
Loose or faulty spreaders, locks, other materials.
Notes: Discuss different areas of a ladder to inspect prior to use. Look for damaged rungs, feet, missing connectors, rot or decay, broken rails and missing identification labels.

## Slide 65: Job-Made Wooden Ladders
Job-made wooden ladders are permissible, if constructed according to OSHA and ANSI specifications.
  Must be constructed to ANSI A14.4-2009 standard.
  Standard contains very specific requirements for type of materials to use, as well as spacing and limitations.
  Do not use job-made ladders unless you have reviewed the OSHA and ANSI regulations and standards.
Notes: Discuss that job-made ladders are permissible, but must be made pursuant to specific OSHA and ANSI requirements. These standards contain specific instructions for the type of materials to use, spacing and limitations of job-made ladders.

## Slide 66: Damaged Ladder Photos
This ladder shows the use of 2x4 wood to repair damaged side-rails and feet of a ladder.
  This ladder should be tagged and removed from service.
Notes: This photo shows a ladder with a 2x4 used to repair the siderail, which is not permitted. Ladders that are damaged must be tagged and removed from service. Also, notice the lumber used to support the bottom step.

## Slide 67: Damaged Ladder Photos, continued 1
The side-rail of this ladder is dented.
  This ladder should be tagged and removed from service.
Notes: The slide shows a photo of a damaged ladder siderail. This ladder should be tagged and removed from service.
Source: http://osha.oregon.gov/OSHAResourceNewsletter/2013/08-2013/images/ladder/fig-03.jpg

## Slide 68: Ladder Labels
Check the labels to learn about:
  Warnings
  Duty rating
  Set-up
Notes: Ladder manufacturers must affix labels which show warnings, duty rating and discuss proper set-up.

## Slide 69: Ladder Setup - Placement
Avoid setting up a ladder in high traffic areas or barricade areas around ladder.
Do not use metal or aluminum ladders near electrical lines.
Place ladders on stable and level surfaces.
Notes: Avoid setting up ladders in a high traffic area or barricaded areas. Do not use metal or aluminum ladders near electrical lines. Additionally, ladders must be placed on stable and level surfaces.

## Slide 70: Ladder Setup – Proper Pitch
Example:
20 ft. (ladder length) ÷ 4 ft. = 5 ft. pitch
Extension ladders should be used at a 4 to 1 pitch (1.2 to .3 m).
For every 4 ft.. (1.2 m) of ladder length, the bottom of the ladder should be 1 ft. (.3 m) away from the structure.
Notes: A good rule of thumb to determine if the ladder is at the proper pitch is to stand at the base of the ladder and extend your arms. If you can touch the ladder while standing straight up the pitch is approximately 4:1.

## Slide 71: Correct Pitch?
Remember, for every 4 ft. (1.2 m) in height, the bottom of the ladder should be 1 ft. (.3 m) away from the structure.
Notes: Discuss the unsafe work practices utilized in this photo. A worker is shown climbing an extension ladder leaning against a residential home under construction at an improper pitch.

## Slide 72: Identify the Hazards
How many hazards do you see in this photo?
Notes: A ladder is shown at an improper angle. Additionally, a stepladder is shown without being fully opened.

## Slide 73: Identify the Hazards, continued 1
How many hazards do you see in this photo?
Notes: A job-made wooden ladder is shown over a floor opening. Floor openings should be properly secured with a cover suitable to handle 2-times the maximum intended load.

## Slide 74: Stepladders
Most stepladders are designed for use in an opened-and-locked position.
Do not use a stepladder that is folded or in a leaning position, unless designed to be leaned directly against a vertical surface.
Notes: Stepladders are only to be used in an opened and locked position. Do not use a stepladder leaning against a structure or in a folded position.

## Slide 75: Stepladders, continued 1
Photos courtesy: Werner Ladder
A standard step ladder and leaning ladder all-in-one.

## Slide 76: Stepladders, continued 2
Never stand on the top 2 steps of a stepladder.
Notes: Never stand on the top 2 rungs of a stepladder as you are at a higher risk to lose your balance and fall.

## Slide 77: Identify the Hazards, continued 3
How many hazards do you see in these photos?
Notes: These photos show employees improperly using stepladders. One worker is shown using a stepladder in a leaning position and the other worker is shown on the top rung of a stepladder.

## Slide 78: Secure and Stabilize Ladders
Secure extension ladders at the top or bottom to prevent movement.
The base of an extension ladder must be secured in place by using the safety feet on the ladder or other effective means.
Notes: Ladders should be secured at the top and bottom to prevent movement or displacement. The base of an extension ladder must be secured by using the feet on the ladder or by other effective means.

## Slide 79: Ladder Secured at the Top
Notes: These photos show two types of ways to secure ladders at the top to prevent displacement. The photo on the left shows a brace or bracket system and the photo on the right shows a chain.

## Slide 80: Ladder Secured at the Bottom
Notes: These photos show examples of ways to secure ladders at the bottom or base. Beyond securing the feet of a ladder into the ground, you can also use an anchor type device, as shown on the photos.

## Slide 81: Securing Ladders in Loose Soil
Dig feet/cleat of extension ladder into soil.
  The feet should face outward and dig into the ground to prevent ladder from kicking out.
Notes: On loose soil or a soft base, dig feet into the ground. The feet should face outward and dig into the ground to prevent the ladder from kicking out.

## Slide 82: Securing Ladders on Firm Base
Use anti-slip shoes/ safety feet on firm ground.
Install a kick-plate or have someone hold the ladder while in use.
Notes: On a firm base, set feet level and on the rubber pads. You can also install a kick-plate or have someone hold the ladder to prevent it from slipping out when in use.

## Slide 83: Identify the Hazards, continued 4
How many hazards do you see in these photos?
Notes: This photo shows improper and unsafe ways to stabilize a ladder on an uneven surface. In these photos buckets are used on stairs to assist in leveling a ladder. This is an unsafe practice and is against OSHA regulations, specifically those found in 29 CFR 1926.1053.

## Slide 84: Securing Ladders on Uneven Surfaces
When the surface is not level, use a ladder leveler (accessory) to provide even contact points.
Notes: To assist in leveling ladders on uneven surfaces, you should use an approved ladder leveling accessory; an example of which is shown in the slide.

## Slide 85: Fiberglass Podium Ladder – Type 1
Notes: 250-lb weight rating.
4, 5 and 6 ft. models
Lightweight, slim profile

## Slide 86: Adjustable Safety Cage Ladder – Type 1AA
Notes: Made from high-strength fiberglass-resin composite.
Non-conductive.
Worker is protected from full enclosed work platform.
Can work hands free within their workspace.

## Slide 87: Multi-use Ladder – Type 1A
Notes: Work safely on uneven terrain.
Wide-based.
Multi-height extension ladder.

## Slide 88: Fiberglass Extension Ladder with Outriggers – Types 1A & 1AA
Notes: Offers a leveling outrigger system that doubles the width of the ladder’s base while increasing its side-tip stability.
Very light compared to other extension ladders.
This model features a side to side bubble level and front-to-back angle indicator, which assists in setting up the ladder safely.

## Slide 89: Safely Working from Ladders
Face the ladder when ascending or descending.
Keep your body centered on the ladder.
Never let your belt buckle pass either ladder side-rail.
Notes: When working from a ladder:
Face the ladder when ascending or descending.
Keep your body centered on the ladder.
Never let your belt buckle pass either ladder side-rail.

## Slide 90: Safely Working from Ladders, continued 1
Maintain three points of contact when ascending or descending a ladder.
Notes: When working from ladders it is important to maintain three points of contact when ascending or descending a ladder. In the photo, a worker is shown with both feet firmly affixed to the ladder and also one hand used as support.
Photo from http://www.orosha.org/resource-newsletter/2013/08-2013/Feat01.html#.VLKkbSvF9qU

## Slide 91: Safely Working from Ladders, continued 2
Remember:
Maintain three points of contact when ascending or descending.
Secure the ladder at the top or bottom.
Extend the ladder at least 3 feet above the level being accessed.
Notes: Recap important ladder safety tips:
Maintain three points of contact when ascending or descending ladder.
Secure the ladder at the top or bottom.
Extend the ladder at least 3 feet above the level being accessed.

## Slide 92: Safely Working from Ladders, continued 3
Do not overreach when working from the ladder.
Do not stand on the top two rungs of a stepladder.
Do not allow another person on a ladder at any given time, unless you are using a double-cleated ladder that is intended for two-way traffic.
Notes: Recap important ladder safety tips:
Do not overreach when working from the ladder.
Do not stand on the top two rungs of a stepladder.
Do not allow another person on a ladder at any given time, unless you are using a double-cleated ladder that is intended for two-way traffic.

## Slide 93: Safely Working from Ladders - Review
Do not carry anything that may cause loss of balance.
Consider using rope to raise/lower material.
Do not stand on top 2 rungs of stepladder.
Use a pulley system to get materials to your working level.
Notes: Recap important ladder safety tips:
Do not carry anything that may cause loss of balance.
Consider using rope to raise/lower material.
Do not stand on top 2 rungs of stepladder.
Use a pulley system to get materials to your working level.

## Slide 94: Section 3
SCAFFOLDS

## Slide 95: Disclaimer
This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.
This presentation is intended to discuss Federal Regulations only - your individual State requirements may be more stringent as many states operate their own state OSHA and they may have adopted construction standards that are different from information presented in this training. If you live in a state with an OSHA approved state plan, you should contact your local administrator for further information on the standards applicable in your state.
These materials are meant for informational purposes only.
No representation is made as to the thoroughness of the presentation.
Notes: This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 96: Disclaimer, continued 1
It is not the intent to provide compliance-based training in this presentation, the intent is more to address hazard awareness in the residential construction (i.e. home building) industry, and to recognize the overlapping hazards present in many construction workplaces.
Photos shown in this presentation may depict situations that are not in compliance with applicable OSHA/safety requirements.
No legal advice is offered or implied, and no attorney-client relationship is intended or established. If legal advice or other expert assistance is required the services of a competent professional person should be sought.
It is the responsibility of the employer and its employees to comply with all pertinent OSHA/safety rules and regulations in the jurisdiction in which they work.
Notes: Please read the disclaimer for legal purposes, this is required under the Susan Harwood Training Grant program.

## Slide 97: Copyright Information © 2018
This material is the copyrighted property of the Job-Site Safety Institute and the National Association of Home Builders. By federal regulation, OSHA reserves a license to use and disseminate such material for the purpose of promoting safety and health in the workplace. The Job-Site Safety Institute and the National Association of Home Builders hereby authorizes employers and workplace safety and health professionals to use this material, distributed by or through OSHA, in their workplaces or practices in accordance with the guidance contained in the material.
To this end, permission is granted to use such copyrighted material solely for non-commercial, instructional, personal, or scholarly purposes. The material may be used and incorporated into other workplace safety and health programs on the condition that no fee may be charged for the subsequent use of the material. Use of the material for any other purpose, particularly commercial use, without the prior, express written permission of the copyright owner/s is prohibited. Furthermore, any modification to the material is prohibited without the prior, express written permission of the copyright owners.
Notes: Note that the these materials are copyrighted by the Job-Site Safety Institute and the National Association of Home Builders. Permission is granted to use such copyrighted material in accordance with the terms on the slide.

## Slide 98: Learning Objectives: Section 3
Identify general requirements for safely building and using scaffolds.
Identify competent person responsibilities.
How to access scaffolds safely.
Determine proper fall protection including guardrails and personal fall arrest systems.
Identify safety requirements applicable to specific types of scaffolds.
Notes: Discuss the learning objectives for Section 3. In this section we will address ladder and scaffold safety, including:
Identify safety requirements and practices for scaffolding, including aerial lifts.

## Slide 99: Scaffolds

## Slide 100: Scaffolding
A safe alternative to using ladders is to use:
Interior and Exterior Scaffolding
Aerial Lifts
...if OSHA requirements and safety practices are followed.
Notes: A safer alternative to working from a ladder is to use interior and exterior scaffolding or aerial lifts.

## Slide 101: Types of Scaffolding
Three basic types:
Supported scaffolds -- platforms supported by rigid, load bearing members, such as poles, legs, frames, & outrigger.
Suspended scaffolds -- platforms suspended by ropes or other non-rigid, overhead support.
Aerial Lifts -- such as “cherry pickers” or “boom trucks”.
Notes: There are three basic types of scaffolding, including:
Supported scaffold
Suspended scaffold
Aerial lifts

## Slide 102: Competent Person Requirements
Designated by the employer.
Has the knowledge and experience required to identify existing and predictable hazards.
Has authority to eliminate unsafe working conditions.
Has authority to stop work if unsafe conditions exists.
Notes: A competent person plays an important role when working on or around scaffolds. A competent person is:
Designated by the employer.
Has the knowledge and experience required to identify existing and predictable hazards.
Has authority to eliminate unsafe working conditions.
Has authority to stop work if unsafe conditions exists.

## Slide 103: Competent Person Requirements, continued 1
Train employees who erect, dismantle, move, or alter scaffolds.
Determine if it is safe for employees to work on or from a scaffold during storms or high winds.
Inspect scaffolds and scaffold components for visible defects before each work shift.
Notes: A competent person is responsible to:
Train employees who erect, dismantle, move, or alter scaffolds.
Determine if it is safe for employees to work on or from a scaffold during storms or high winds.
Inspect scaffolds and scaffold components for visible defects before each work shift.

## Slide 104: Scaffold Inspection
Competent person inspects scaffolds for visible defects before each shift and after any alterations
Defective parts must be immediately repaired
Notes: Before each shift, and after any alterations, a competent person must inspect the scaffold for visible defects. Any defective parts must be immediately repaired.
Photo courtesy of OSHA.

## Slide 105: Types of Common Scaffolds
Fabricated Frame Scaffold
Notes: The photo shows a fabricated frame scaffold.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 106: Types of Common Scaffolds, continued 1
Pump-Jack Scaffold
Notes: The photo shows an example of a pump-jack scaffold.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 107: Types of Common Scaffolds, continued 2
Ladder-Jack Scaffold
Notes: This photo shows an example of a ladder-jack scaffold.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 108: Types of Common Scaffolds, continued 3
Interior-Mobile Scaffold
Notes: This photo shows an example of an interior mobile scaffold.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 109: Types of Common Scaffolds, continued 4
Trestle Scaffold
Notes: This photo shows an example of a trestle scaffold.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 110: Types of Common Scaffolds, continued 5
Top-Plate Scaffold
Notes: This photo shows an example of a top plate scaffold. This type of scaffold can be used to set floor joists, or roof joists.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 111: Interior and Exterior Scaffolding
Job-built scaffolding that is improperly constructed is extremely hazardous.
Various types and brands of interior and exterior scaffolding are commercially available.
  Always, follow the manufacturer’s safety instructions.
Notes: Discuss the hazards associated with improperly constructed job-built scaffolds, and the types of interior and exterior scaffolding that is commercially available. It is important to always follow the manufacturer’s safety instructions regarding proper setup and use.

## Slide 112: Common Hazards on Jobsites
Defective wood planks and inadequate planking overhang.
Unsafe access to scaffold.
Cross bracing not adequate.
Inadequate footings.
Bridging of scaffolds.
Working within 10 feet of overhead power lines (discuss in greater detail)
Notes: Discuss examples of common scaffold hazards on jobsites; which include:
Defective wood planks and inadequate planking overhang.
Unsafe access to scaffold.
Cross bracing not adequate.
Inadequate footings.
Bridging of scaffolds.
Working within 10 feet of overhead power lines (discuss in greater detail)

## Slide 113: Training Requirements
All employees must be trained prior to working on scaffolds.
Qualified person must conduct the training and include the following:
  Electrical Hazards
  Fall Protection
  Falling Object Protection
  Proper Use
  Material Handling
  Load-carrying Capacities
Notes: All employees working on a scaffold must be trained. Training should be conducted by a qualified person and include training on electrical hazards, fall protection, falling object protection, proper use, material handling and load-carrying capacities.

## Slide 114: Basic Requirements
Scaffolding that is more than 10 ft. or higher must be equipped with guardrails.
A competent person must supervise the set-up and take down of all scaffolding.
Scaffolding must be fully planked, and planks must be secured so they cannot move.
Notes: The trigger height for when guardrails must be used on a scaffold is 10 feet. Additionally, a competent person must supervise the setup and take down of all scaffolding. The working deck of a scaffold must be fully planked, and the planks must be secured to prevent movement.

## Slide 115: Basic Requirements, continued 1
Erect/dismantle all scaffolds according to the manufacturer's Instructions
Capacity
    Must support 4x Intended Load
Stable Footings
    Base Plate, Screw Jacks & Mudsills
Notes: Scaffolds must be capable of supporting 4 times the maximum intended load. Additionally, scaffolds must be placed on stable footings with a proper base plate, screw jacks and mudsills.

## Slide 116: Basic Requirements, continued 2
Scaffolds must be capable of supporting its own weight and at least 4 times the anticipated load.
Expected load includes:
    Workers
    Equipment
    Tools
    Materials
Notes: When calculating the anticipated load, factor in the weight of workers, equipment, tools and any materials being placed on the scaffold.

## Slide 117: Requirements on Jobsites
Front edge of all platforms must be within 14” of face of work (i.e., structure).
Notes: The front edge of all platforms must be within 14” of the face of the work or structure.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 118: Requirements on Jobsites, continued 1
Planks – must extend 6’’ to 12” past the end of supports or be cleated.
Notes: Ends of platforms must extend at least 6” over the center line of the support, if not equipped with cleats or hooks to prevent movement.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 119: Requirements on Jobsites, continued 2
Base Plate & Mudsill are Required
Notes: Base plates and mudsills are required.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 120: Requirements on Jobsites, continued 3
Masonry Bricks & Blocks are not acceptable scaffold bases.
Notes: Masonry bricks and blocks are not acceptable scaffold bases.
Photo provided by SEE, Inc.

## Slide 121: Requirements on Jobsites, continued 4
Each platform on all working levels must be fully planked and secured to prevent movement.
No more than a 1” space between decking/platform units and upright supports.
Wood scaffold planks must be nominal 2” x 10”.
Must be Scaffold Grade Planks or equivalent.
Notes: Each platform on all working levels must be fully planked and secured. There should be no more than a 1” space between decking and planking should be nominal 2” x 10” and made of scaffold grade planks.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 122: Scaffold Access
Ladders needed if access to scaffold is more than 2 feet.
Do not climb cross bracing.
Place ladders securely.
  Ladders must be positioned so they will not tip the scaffold.
OSHA permits direct access from another scaffold, structure, or personnel hoist.
Notes: A ladder must be used when accessing a scaffold more than 2’ off the ground. Do not climb cross bracing.

## Slide 123: Scaffold Access, continued 1
Ladders needed if access to scaffold is more than 2 feet.
Notes: This photo shows a ladder placed against a fabricated frame scaffold to allow workers to access the working level safely.

## Slide 124: Guardrail Requirements- Scaffolds
Toprails Between 38” and 45” High
Guardrails to 200 lbs/Midrails to min. 75 lbs – 150 lbs depending on Toprail capacity.
Cross Bracing OK as Guardrail if Between 20” and 30” for Midrail; 38” to 48” for Toprail
Protect from Falling Objects
  All Workers on Scaffolds MUST Wear Hard Hats
Notes: Discuss the requirements for guardrails on scaffolding.
OSHA states that the top edge height of toprails or equivalent member on supported scaffolds manufactured or placed in service after January 1, 2000 shall be installed between 38 inches (0.97 m) and 45 inches (1.2 m) above the platform surface. The top edge height on supported scaffolds manufactured and placed in service before January 1, 2000, and on all suspended scaffolds where both a guardrail and a personal fall arrest system are required shall be between 36 inches (0.9 m) and 45 inches (1.2 m).
Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members of a guardrail system shall be capable of withstanding, without failure, a force applied in any downward or horizontal direction at any point along the midrail or other member of at least 75 pounds (333 n) for guardrail systems with a minimum 100 pound toprail capacity, and at least 150 pounds (666 n) for guardrail systems with a minimum 200 pound toprail capacity.

## Slide 125: Cross Bracing OK as Top Rail
Midrail
Toprail
Cross Bracing OK as Toprail
Notes: Overall, a pretty well built stucco scaffold with proper guardrails.
Braces are used as top rails with midrails installed approximately half way
Discuss the requirements for guardrails on scaffolding.
OSHA states that the top edge height of toprails or equivalent member on supported scaffolds manufactured or placed in service after January 1, 2000 shall be installed between 38 inches (0.97 m) and 45 inches (1.2 m) above the platform surface. The top edge height on supported scaffolds manufactured and placed in service before January 1, 2000, and on all suspended scaffolds where both a guardrail and a personal fall arrest system are required shall be between 36 inches (0.9 m) and 45 inches (1.2 m).
Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members of a guardrail system shall be capable of withstanding, without failure, a force applied in any downward or horizontal direction at any point along the midrail or other member of at least 75 pounds (333 n) for guardrail systems with a minimum 100 pound toprail capacity, and at least 150 pounds (666 n) for guardrail systems with a minimum 200 pound toprail capacity.

## Slide 126: Identify the Hazards
How many hazards do you see in this photo?
Notes: This photo shows multiple unsafe practices, such as installing a scaffold on improper footing without the use of mudsills. Scaffolds should not be placed on blocks.

## Slide 127: Identify the Hazards, continued 1
How many hazards do you see in this photo?
Notes: Discuss the various safety hazards shown in this photo. Examples of these hazards include:
Improper planking
Overloading of scaffold
Improper footing
Improper use of mudsills

## Slide 128: Identify the Hazards, continued 2
How many hazards do you see in this photo?
Notes: Discuss the various safety hazards shown in this photo.

## Slide 129: Identify the Hazards, continued 3
How many hazards do you see in this photo?
Notes: Discuss the various safety hazards shown in this photo.

## Slide 130: Identify the Hazards, continued 4
How many hazards do you see in this photo?
Notes: Discuss the various safety hazards shown in this photo. Examples of these hazards include:
Improper planking
Overloading of scaffold

## Slide 131: Identify the Hazards, continued 5
How many hazards do you see in this photo?
Notes: Discuss the various safety hazards shown in this photo.

## Slide 132: Identify the Hazards, continued 6
How many hazards do you see in this photo?
Notes: Discuss the various safety hazards shown in this photo. Examples of these hazards include:
Improper planking
Improper footing
Improper use of mudsills

## Slide 133: Identify the Hazards, continued 7
How many hazards do you see in this photo?
Notes: Discuss the various safety hazards shown in this photo.

## Slide 134: Identify the Hazards, continued 8
How many hazards do you see in this photo?
Notes: Discuss the various safety hazards shown in this photo.

## Slide 135: Identify the Hazards, continued 9
Notes: Planks with visible defects, such as bowing and cracks (as shown in this slide) must not be used.

## Slide 136: Identify the Hazards, continued 10
Notes: Planks with visible defects, such as bowing and cracks (as shown in this slide) must not be used.

## Slide 137: Identify the Hazards, continued 11
Notes: There are many hazards associated with using job-made scaffolds, including the lack of available engineering data to show the maximum intended load. Only use approved scaffolding material on a jobsite. This photo shows worker using a job-made scaffold, which is unsafe and could cause a worker to experience a fatal fall.

## Slide 138: Safe Practices - Fully Planked Scaffold
Notes: This picture shows a fully planked scaffold complete with a kick-plate.

## Slide 139: Safe Practices – Pump-Jack Scaffold
Notes: This photo shows a properly used pump jack scaffold.

## Slide 140: PFAS Used with Ladder Jack Scaffold
Notes: Ladder jack scaffolds cannot exceed 20ft and workers must use a PFAS if they are working higher than 10ft.

## Slide 141: Aerial Lifts
Aerial lifts (e.g., JLG boom lift) or approved personnel lift baskets on rough terrain forklifts is a safe alternative to working from:
    Ladders, or
    other types of scaffolding.
An aerial lift can be used for the installations of:
    windows
    soffit
    fascia
    gutters
    siding
Notes: Aerial lift can be a safe alternative to working from ladders or other forms of scaffolding. These lifts can be used for a variety of tasks including the attachment of exterior fixtures or accessories.

## Slide 142: Aerial Lifts, continued 1
Notes: Picture of an aerial lift on a residential construction jobsite.

## Slide 143: Aerial Lifts, continued 2
Notes: Picture showing a personnel basket attached to a forklift (left) and the use of a PFAS attached to an anchor point on an aerial lift (on the right).
A personnel basket attached to a forklift must be approved by the forklift manufacturer or by a registered professional engineer.

## Slide 144: Aerial Lifts, continued 3
The competent person should:
Restrict operation of aerial lifts or forklift vehicles to trained and authorized personnel.
Use only commercially built personnel baskets designed for lifting workers.
  Follow the American National Standards Institute’s (ANSI) standards for using personnel lift baskets.
Make certain that homemade boxes lifted by a forklift are not used—homemade boxes are unacceptable.
Notes: Aerial lift competent person requirements:
Restrict operation of aerial lifts or forklift vehicles to trained and authorized personnel.
Use only commercially built personnel baskets designed for lifting workers.
Follow the American National Standards Institute’s (ANSI) standards for using personnel lift baskets.
Make certain that homemade boxes lifted by a forklift are not used—homemade boxes are unacceptable.

## Slide 145: Aerial Lifts, continued 4
When in the lift:
Wear a full body harness.
Attach the lanyard to the boom or an approved anchor point inside the basket.
Notes: When working from an aerial lift, remember to always wear a full body harness and attach and approved lanyard to the boor or approved anchor point inside the basket.

## Slide 146: Proper use of PFAS in Basket
Notes: Close-up picture of a worker using an aerial lift (using a PFAS).

## Slide 147: Aerial Lifts, continued 5
When in the lift:
Always stand on the floor of the basket.
Do not sit or climb on the edge of the basket, lean over the edge, or climb out of the basket.
Do not use a ladder or other objects to increase reach.
Notes: Always stand on the top floor of the basket and do not sit or climb on the edge of the basket, lean over the edge or climb out of the basket. Do not use a ladder or other objects to increase your reach.

## Slide 148: Aerial Lifts, continued 6
When operating the lift:
Stay at the controls at all times.
Do not move the vehicle while a person is in the elevated basket.
Only use the equipment when it is on stable and level ground.
Maintain the required minimum clearance of 10 ft. (3 m) from power lines carrying 50 kilovolts or less.
Notes: When operating an aerial lift, stay in control of the lift at all times and do not move the vehicle with a person inside the basket. Additionally, only use the equipment when it is on a stable and level ground. Remember – it is important to maintain the minimum clearance distance of 10 feet from all power lines.
***Please note that the clearance distances from overhead power lines may change.

## Slide 149: Why a harness is necessary.
Notes: Picture showing a worker that has fallen out of lift basket and is restrained by his harness attached to the anchor point of the lift.

## Slide 150: Section 4
Conventional Fall Protection

## Slide 151: Disclaimer
This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.
This presentation is intended to discuss Federal Regulations only - your individual State requirements may be more stringent as many states operate their own state OSHA and they may have adopted construction standards that are different from information presented in this training. If you live in a state with an OSHA approved state plan, you should contact your local administrator for further information on the standards applicable in your state.
These materials are meant for informational purposes only.
No representation is made as to the thoroughness of the presentation.
Notes: This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 152: Disclaimer, continued 1
It is not the intent to provide compliance-based training in this presentation, the intent is more to address hazard awareness in the residential construction (i.e. home building) industry, and to recognize the overlapping hazards present in many construction workplaces.
Photos shown in this presentation may depict situations that are not in compliance with applicable OSHA/safety requirements.
No legal advice is offered or implied, and no attorney-client relationship is intended or established. If legal advice or other expert assistance is required the services of a competent professional person should be sought.
It is the responsibility of the employer and its employees to comply with all pertinent OSHA/safety rules and regulations in the jurisdiction in which they work.
Notes: Please read the disclaimer for legal purposes, this is required under the Susan Harwood Training Grant program.

## Slide 153: Copyright Information © 2018
This material is the copyrighted property of the Job-Site Safety Institute and the National Association of Home Builders. By federal regulation, OSHA reserves a license to use and disseminate such material for the purpose of promoting safety and health in the workplace. The Job-Site Safety Institute and the National Association of Home Builders hereby authorizes employers and workplace safety and health professionals to use this material, distributed by or through OSHA, in their workplaces or practices in accordance with the guidance contained in the material.
To this end, permission is granted to use such copyrighted material solely for non-commercial, instructional, personal, or scholarly purposes. The material may be used and incorporated into other workplace safety and health programs on the condition that no fee may be charged for the subsequent use of the material. Use of the material for any other purpose, particularly commercial use, without the prior, express written permission of the copyright owner/s is prohibited. Furthermore, any modification to the material is prohibited without the prior, express written permission of the copyright owners.
Notes: Note that the these materials are copyrighted by the Job-Site Safety Institute and the National Association of Home Builders. Permission is granted to use such copyrighted material in accordance with the terms on the slide.

## Slide 154: Learning Objectives: Section 4
Identify when fall protection is required.
Identify types of “conventional” fall protection systems.
Determine which protection system to use for a given fall hazard.
Identify key requirements and basic safety practices for each protection system.
Notes: Discuss the learning objectives for Section 4. In this section we will address conventional fall protection systems, including:
Identify when fall protection is required.
Identify types of “conventional” fall protection systems.
Determine which protection system to use for a given fall hazard.
Identify key requirements and basic safety practices for each protection system.

## Slide 155: When is Fall Protection Required?
OSHA §1926 Subpart M
Where workers on a residential construction site are exposed to vertical drops of 6 feet or more, OSHA requires that employers provide fall protection in one of three ways before work begins:
1) Conventional Fall Protection
2) Other Work Methods (Section 2)
3) Non-Conventional Fall Protection (Section 4)
Notes: Discuss that OSHA’s fall protection regulation is found in 29 Code of Federal Regulations 1926 Subpart M. When workers are exposed to fall hazards 6 feet or more, OSHA requires the use of conventional fall protection, other work methods or alternative fall protection.

## Slide 156: Requirements on Jobsites
Approved OSHA State Plans
Some OSHA State-Plan states may have different trigger heights of when conventional fall protection is required on residential jobsites.
These states include, but may not be limited to:
  California
  Kentucky
  North Carolina
  Arizona
  Washington
  Oregon
Notes: Discuss that some OSHA State-Plan states may have different trigger heights of when conventional fall protection is required on residential jobsites. Participants should refer to their state-plan requirements to understand if they have different requirements from federal OSHA.

## Slide 157: What is Conventional Fall Protection?
3) Personal Fall
Arrest System
(PFAS)
2) Safety Nets
1) Guardrails
Notes: OSHA identifies guardrails, safety nets and personal fall arrest systems as the three types of conventional fall protection.

## Slide 158: Guardrail Systems
Barrier built to OSHA specifications; constructed to prevent workers from falling to lower levels
Protects against these hazards:
  Window and Wall Openings
  Unprotected Sides and Edges
  Floor Holes
Notes: A guardrail is a barrier built to OSHA specifications and is constructed to prevent workers from falling to lower levels. They can be used to protect against window and wall openings, unprotected sides and edges and floor hole hazards.

## Slide 159: Guardrail Systems Are Needed For:
Stairwell Openings
Open-sided Wall Openings
Second and Third Story Non-loading Bearing Walls When the Studs Are 24” OC
Low (Less Than 39”) Silled Windows
Second and Third Story Deck Floor Holes for Open Foyers or Cat Walks
Sliding Glass and French Door Openings Onto Decks and Porches
Skylight Openings Cut Into the Roof
Notes: Guardrails can be used to protect workers from falling during many stages of the residential construction process. This slide shows a variety of hazards that guardrails can be used to protect workers from falls.

## Slide 160: Height Requirements for Guardrails
  Toprail
    42 in. ± 3 in. (1.1 m)
  Midrail
    21 in. ± 3 in. (50 cm)
  Toe Board
    Minimum of 3 ½ in. (4 in. nominal) (10.2 cm)
Notes: When constructing a guardrail, the toprail should be 42 inches, plus or minus 3 inches; the midrail 21 inches, plus or minus 3 inches; and the toeboard a minimum of 3 ½ inches.

## Slide 161: Requirements for Guardrails
Vertical Supports
  Install no more than every 8 ft. (2.4 m)
Weight Requirement
  Must support at least 200 lbs. (90.9 kg) of force outward and downward along top edge
Notes: Vertical supports on guardrails must be placed no more than every 8 feet apart. Guardrails must be able to support at least 200 pounds of force outward and downward along the top edge.

## Slide 162: Properly installed guardrail system
Top-rail @ 42” ± 3”
Mid-rail @ 21” ± 3”
Toeboard min. 3-1/2”
Notes: This photo shows a properly installed guardrail system around a stairwell opening.
Top-rail = 42in.
Mid-rail = 21in.
Toeboard = 3 ½ in. (4in. Nominal)

## Slide 163: Guardrail Uses in Residential Construction
Wall Openings
  Wall openings greater than 18” need to be protected.
Notes: This photo shows a properly constructed guardrail used to protect a wall opening greater than 18 inches.

## Slide 164: Guardrail Uses in Residential Construction, continued 1
Wall Openings
  Wall openings greater than 18” need to be protected.
Notes: This photo shows missing guardrails on a wall opening greater than 18 inches. Guardrails were drawn-in to show the approximate location where they should be installed.

## Slide 165: Guardrail Uses in Residential Construction, continued 2
Wall Openings
  Wall openings greater than 18” need to be protected.
Notes: This photo shows a properly constructed guardrail used to protect a wall opening greater than 18 inches.

## Slide 166: Guardrail Uses in Residential Construction, continued 3
Wall Openings
  Wall openings greater than 18” need to be protected.
Notes: This photo shows a properly constructed guardrail used to protect a wall opening greater than 18 inches.

## Slide 167: Guardrail During Drywall Installation
Prevent the need to remove guardrails during drywall installation:
  Build guardrail uprights 6 to 12 in. (15.4 to 30.5 cm) away from where drywall will be placed
Notes: When guardrails are needed to protect wall openings, and drywall has to be installed, consider using a safety-boot system such as the example on the next slide.

## Slide 168: Guardrail Uses in Residential Construction, continued 4
Wall Openings even when Drywall is Installed.
Notes: This photo shows a properly constructed guardrail used to protect a wall opening greater than 18 inches.

## Slide 169: Guardrail Uses in Residential Construction, continued 5
24” on Center Studs need Guardrails
Notes: When wall studs are 24 inches on center, guardrails must be used to protect workers from falling through the opening. This photo shows guardrails drawn-in where they should be located.

## Slide 170: Requirement for Window Openings
For all window openings, the sill height determines the need for a guardrail.
Window openings with a 6 ft. fall hazard (1.8 m) require the installation of a guardrail system, if the bottom sill height is less than 39 in. (1.1 m).
Notes: Window openings with a 6ft fall hazard requires the installation of a guardrail system. For window openings, the sill height determines the need for a guardrail.

## Slide 171: Guardrail Uses in Residential Construction, continued 6
Window Openings
  Window openings with a fall hazard and low sill height.
Less than 39”
Notes: The photo shows the approximate location where a guardrail should be placed. Since the window sill height is less than 39 inches, a guardrail is necessary.

## Slide 172: Is a guardrail required?
Notes: Notice the ladder in the background. The use of the ladder near the window opening would require the height of the guardrail to be increased.
Discuss: The worker using the power nailer (nail gun) should be wearing protective eyewear (safety glasses) to protect from any flying object hazards.
In general OSHA requires employees to be protected from any potential eye or face injury from physical hazards.
Note: Safety glasses must meet the requirements specified in American National Standards Institute, Z87.1-1968, Practice for Occupational and Educational Eye and Face Protection.

## Slide 173: Guardrail Uses in Residential Construction, continued 7
Window Openings
  Window openings with a fall hazard and low sill height.
Notes: This photo shows a worker standing on a stepladder and exposed to a fall hazard through a wall opening. There should be a guardrail system installed at the level the workers are working from.

## Slide 174: Guardrail Uses in Residential Construction, continued 8
Window Openings
  Window openings with a fall hazard and low sill height.
Notes: This photo shows the correct use of guardrails to protect workers from falling through wall openings.

## Slide 175: Guardrail Uses in Residential Construction, continued 9
Window Openings
  Window openings with a fall hazard and low sill height.
Notes: This photo shows a residential home under construction with some wall and window openings with guardrails installed, and some without.

## Slide 176: Guardrail Uses in Residential Construction, continued 10
Window Openings
  Window openings with a fall hazard and low sill height.
Notes: This photo shows a guardrail installed on a window opening with a window sill height less than 39 inches.

## Slide 177: Guardrail Uses in Residential Construction, continued 11
Floor Openings
  Guardrails can be used to protect unguarded floor openings.
Notes: The photos in the slide show unguarded floor openings. Guardrails can be used to protect workers from falling through unguarded floor holes or openings.

## Slide 178: Guardrail Uses in Residential Construction, continued 12
Stair Openings
  Guardrails can be used to protect unguarded stair openings.
Notes: The photos in the slide show unguarded stair openings. Guardrails can be used to protect workers from falling through unguarded stair holes or openings.

## Slide 179: Guardrail Uses in Residential Construction, continued 13
Stair Openings
  Guardrails can be used to protect unguarded stair openings.
Notes: The photos in the slide show unguarded stair openings. Guardrails can be used to protect workers from falling through unguarded stair holes or openings.

## Slide 180: Guardrail Uses in Residential Construction, continued 14
Rear Door Openings
  Guardrails can be used to protect unguarded doorways.
Notes:   Guardrails can be used to protect unguarded doorways.

## Slide 181: Guardrail Uses in Residential Construction, continued 15
Rear Door Openings
  Guardrails can be used to protect unguarded doorways.
Notes: These photos show temporary and permanent guardrails placed at the location of doorways with fall hazards present.

## Slide 182: Guardrail Uses in Residential Construction, continued 16
Protect Elevated Workers
  When workers are using stilts, increase the height of the top edge of the top rail to the amount equal to height of stilts.
Notes:   When workers are using stilts, increase the height of the top edge of the top rail to the amount equal to height of stilts.

## Slide 183: Guardrail Uses in Residential Construction, continued 17
Completed decks
Lofts
Stair landings
Ramps or runways
Open-sided balconies and platforms
Notes: Guardrails can be used to protect workers on decks, lofts, stair landings, ramps and open-sided balconies.

## Slide 184: Guardrail Uses in Residential Construction, continued 18
Open-Sided Balcony and Platforms
Notes: Guardrails can be used to protect workers from falling through an open-sided balcony and platform. This photo shows the approximate location where guardrails can be located.

## Slide 185: Guardrail Uses in Residential Construction, continued 19
Open-Sided Balcony and Platforms
Greater Than 6’ Fall
Notes: Guardrails can be used to protect workers from falling through an open-sided balcony and platform. This photo shows the approximate location where guardrails can be located.

## Slide 186: Safety Nets
System consisting of connectors and net installed below a working surface; designed to prevent a worker from contacting a lower level or structure in the event of a fall.
Notes: Safety nets consist of connectors and net installed below a working surface; designed to prevent a worker from contacting a lower level or structure in the event of a fall.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration

## Slide 187: Safety Nets, continued 1
When used, safety must extend 8 feet beyond the edge of the work surface where employees are exposed and be installed as close under the work surface as practical but in no case more than 25 feet below.
Safety nets must be drop-tested at the jobsite after initial installation and before being used as a fall protection system, and at 6-month intervals if left in one place.
Notes: Safety nets must:
Extend 8 feet beyond the edge of the work surface where employees are exposed.
Be installed as close under the work surface as practical but in no case more than 25 feet below.
Be drop-tested at the jobsite after initial installation and before being used as a fall protection system.

## Slide 188: Safety Nets, continued 2
The drop-test consists of a 400 pound bag of sand, that is 28-32 inches in diameter, dropped into the net from the highest walking/working surface at which workers are exposed to fall hazards, but dropped from at least 42 inches above that level.
Notes: Photo from OSHA

## Slide 189: Personal Fall Arrest Systems
Commonly called a (PFAS) it’s comprised of an anchorage point, connectors, and a body harness used together to keep a worker from free falling from an elevated surface.
Notes: A personal fall arrest system (PFAS) is comprised of an anchorage point, connectors, and a body harness used together to keep a worker from free falling from an elevated surface.
Photo courtesy of NAHB.

## Slide 190: Proper PFAS for roofing
Lifeline
Anchor Point
Rope Grab
Full Body Harness
Shock Absorbing Lanyard
Notes: Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration

## Slide 191: Personal Fall Arrest Systems, continued 1
Self-retracting lanyard (SRL)
Rope-grab system
Lifelines can include rope-grab systems or self-retracting lanyards (SRL’s).
Notes: Lifelines can include rope-grab or self-retracting lanyards.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration

## Slide 192: Self-Retracting Lanyards / SRL’s
The availability and lower prices of SRL’s has led to a dramatic increase in their use in recent years.
SRL’s are available for a variety of uses, including leading edge work.
Notes: The lower prices and rising availability of self-retracting lanyards (SRL) has led to a dramatic increase in use in recent years. SRL’s serve a variety of uses to protect workers from falling.

## Slide 193: PFAS – Prior to Use
Review the manufacturer's instructions for proper use, inspection, donning, limitations, accessories, and other information.
Inspect a PFAS prior to EACH USE.
Remember in the event of a fall, this protects your LIFE.
Don’t use a PFAS that is damaged, worn, or has experienced an arrested fall.
Notes: Prior to use, a PFAS should be inspected and damaged, work or components that have experienced an arrested fall should be removed from service. All manufacturer’s instructions should be followed for proper use.

## Slide 194: PFAS Components
D-rings and snaphooks must be capable of withstanding 3,600 lbs. without failure.
Snaphooks must not be attached to:
  Directly to webbing, rope or wire rope
  To each other
  To a D-ring with another snaphook or connector on it
  To a horizontal lifeline
Notes: Components of a PFAS include:
D-rings and snaphooks which must be capable of withstanding 3,600 lbs. without failure.
Snaphooks which must not be attached to:
  Directly to webbing, rope or wire rope
  To each other
  To a D-ring with another snaphook or connector on it
  To a horizontal lifeline

## Slide 195: Inspecting Components of PFAS
Inspecting a harness:
  Inspecting the buckles
  Inspecting the lanyard
  Carefully checking the webbing for distortions
  Check the hardware (D-rings) connectors for defects
  Inspect rope or lifeline for any rips, tears, or deformities
Notes: When inspecting a harness:
  Inspecting the buckles
  Inspecting the lanyard
  Carefully checking the webbing for distortions
  Check the hardware (D-rings) connectors for defects
  Inspect rope or lifeline for any rips, tears, or deformities

## Slide 196: Inspecting PFAS
Quick Tip –
  Many types of harnesses and SRL’s have inspection tags installed on them.
  This makes it easy for you to keep track of the inspections you have performed.
Notes: Many types of harnesses and SRL’s have inspection tags installed on them.

## Slide 197: Wearing a PFAS
Proper wear: locate the D-ring on the back of the harness in the center of the back between the shoulder blades.
Notes: When wearing a PFAS, always remember to locate the D-ring on the back of the harness in the center of the back, between the shoulder blades.

## Slide 198: Wearing a PFAS, continued 1
Proper wear: always adjust the harness to ensure it fits tight to prevent you from falling out of the harness in the event of a fall.
Notes: Always adjust the harness to ensure it fits tight to prevent you from falling out of the harness in the event of a fall.

## Slide 199: Anchor Point Requirements
Anchor points must be capable of supporting 5,000 pounds or the maximum arresting force.
Notes: Anchor points must be capable of supporting 5,000 pounds or twice the intended load.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.
Second photo is directly from Miller Fall Protection by Honeywell. https://www.millerfallprotection.com/smart-solutions/guide-to-fall-protection/personal-fall-arrest-system

## Slide 200: Examples of Anchor Points
Anchor point is installed on a series of braced roof trusses.
Notes: This slide shows a worker installing roof sheathing while wearing a PFAS connected to an anchor point on a series of braced trusses.

## Slide 201: Examples of Anchor Points, continued 1
Anchor point is installed through floor sheathing into floor trusses to support a worker using a leading edge self-retracting lifeline.
Notes: This slide shows a worker using a PFAS attached to a floor-anchor while using a leading edge self-retracting lanyard.

## Slide 202: Anchor Points
A horizontal lifeline is attached to a vertical structural pole and can be used to tie off framers.
Notes: A horizontal lifeline is attached to a vertical structural pole and is a system which can be used to tie off framers.

## Slide 203: Anchor Points, continued 1
A horizontal lifeline is attached to a vertical structural pole and can be used to tie off framers.
Notes: This slide shows workers attached to a horizontal lifeline, which is attached to a vertical structural pole used to tie off framers.

## Slide 204: Examples of Anchor Points
Sample Anchor Points:
Notes: This slide depicts samples of various anchor points.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration.

## Slide 205: Calculating Fall Distances
Regulations require that a worker cannot free fall 6 feet or more.
How far a worker will fall depends on a variety of factors, which include but is not limited to:
  Body size of worker
  Fit of harness, to allow for stretch
  Type of lanyard (rip-stitch or self-retracting)
  Safety factors
Notes: Various factors go into calculating a fall distance, including the height of a worker, fit of harness, type of lanyard and built-in safety factors.

## Slide 206: Calculating Fall Distances, continued 1
Notes: Illustration courtesy of: Miller Fall Protection, Bacou-Dalloz.

## Slide 207: Swing Fall Hazard
A hazard created if a worker is not directly below the anchor point and experiences a fall; which caused the worker to swing back towards the anchor point.
In order to minimize the swing follow a fall:
  Work directly below the anchor.
  Do not extend your work zone more than 30o from the anchor.
  Manage the slack in the rope.
Notes: A swing fall can be created if a worker is not directly below the anchor point and experiences a fall; which caused the worker to swing back towards the anchor point.

## Slide 208: Swing Fall Hazard, continued 1
Notes: To reduce the risk of a swing fall hazard workers should work no more than 30 degrees from an anchor point.

## Slide 209: Swing Fall Hazard
Swing Fall Hazard, continued 2.
Notes: This slide shows a worker exposed to a swing fall hazard.
Photo provided by materials developed through a Susan Harwood Training Grant, a program of the US Department of Labor, Occupational Safety & Health Administration

## Slide 210: Identify the Hazards
How many hazards do you see in this photo?
Notes: This photo shows a worker working at heights above 6 feet without utilizing conventional fall protection.

## Slide 211: Identify the Hazards, continued 1
How many hazards do you see in this photo?
Notes: This photo shows a worker working at heights above 6 feet without utilizing conventional fall protection.

## Slide 212: Identify the Hazards, continued 2
How many hazards do you see in this photo?
Notes: This photo shows stairs with 4 or more risers without proper handrails or guardrails. Additionally there is an unguarded wall opening that Is not protected by guardrails.

## Slide 213: Limitations of using a PFAS
Limitations of conventional fall protection systems during the installation of exterior walls may include:
  Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
  Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Notes: Limitations of conventional fall protection systems during the installation of exterior walls may include the lack of a suitable anchor point or in special instances where the installation of guardrail system could involve more risk, due to the duration of the fall exposure.

## Slide 214: Limitations of using a PFAS, continued 1
  Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
  Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
  Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.

## Slide 215: Recap
In construction, the trigger height for when conventional fall protection (guardrails, PFAS, safety nets) is required is 6 feet.
Before being exposed to fall hazards, workers must be trained.
Understand the proper use and limitations of fall protection systems before beginning work.
Never take shortcuts, always ask for assistance from a supervisor or competent person if you are unsure about a fall hazard or protective system.
Notes: Remember, the trigger height for when conventional fall protection is required is 6 feet. Workers need to be trained before being exposed to fall hazards, and must understand the proper use and limitations of fall protection systems being utilized.

## Slide 216: Section 5
Additional Fall Protection Systems

## Slide 217: Disclaimer
This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.
This presentation is intended to discuss Federal Regulations only - your individual State requirements may be more stringent as many states operate their own state OSHA and they may have adopted construction standards that are different from information presented in this training. If you live in a state with an OSHA approved state plan, you should contact your local administrator for further information on the standards applicable in your state.
These materials are meant for informational purposes only.
No representation is made as to the thoroughness of the presentation.
Notes: This material was produced under the Susan Harwood training grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 218: Disclaimer, continued 1
It is not the intent to provide compliance-based training in this presentation, the intent is more to address hazard awareness in the residential construction (i.e. home building) industry, and to recognize the overlapping hazards present in many construction workplaces.
Photos shown in this presentation may depict situations that are not in compliance with applicable OSHA/safety requirements.
No legal advice is offered or implied, and no attorney-client relationship is intended or established. If legal advice or other expert assistance is required the services of a competent professional person should be sought.
It is the responsibility of the employer and its employees to comply with all pertinent OSHA/safety rules and regulations in the jurisdiction in which they work.
Notes: Please read the disclaimer for legal purposes, this is required under the Susan Harwood Training Grant program.

## Slide 219: Copyright Information © 2018
This material is the copyrighted property of the Job-Site Safety Institute and the National Association of Home Builders. By federal regulation, OSHA reserves a license to use and disseminate such material for the purpose of promoting safety and health in the workplace. The Job-Site Safety Institute and the National Association of Home Builders hereby authorizes employers and workplace safety and health professionals to use this material, distributed by or through OSHA, in their workplaces or practices in accordance with the guidance contained in the material.
To this end, permission is granted to use such copyrighted material solely for non-commercial, instructional, personal, or scholarly purposes. The material may be used and incorporated into other workplace safety and health programs on the condition that no fee may be charged for the subsequent use of the material. Use of the material for any other purpose, particularly commercial use, without the prior, express written permission of the copyright owner/s is prohibited. Furthermore, any modification to the material is prohibited without the prior, express written permission of the copyright owners.
Notes: Note that the these materials are copyrighted by the Job-Site Safety Institute and the National Association of Home Builders. Permission is granted to use such copyrighted material in accordance with the terms on the slide.

## Slide 220: Learning Objectives: Section 5
Identify types of Additional Fall Protection Systems and “alternative” fall protection systems.
Discuss potential uses and limitations of using an “alternative” form of fall protection.
Identify key requirements and basic safety practices for each alternative protection system.
Understand when a written fall protection plan is necessary.
Notes: Discuss the learning objectives for Section 5. In this section we will identify additional fall protection systems as well as “alternative” fall protection. We will also discuss uses and limitations of these types of systems and identify key requirements for each alternative protection system. Lastly, we will understand when a written fall protection plan is necessary.

## Slide 221: Reminder of Conventional Fall Protection
3) Personal Fall
Arrest System
(PFAS)
2) Safety Nets
1) Guardrails
Notes: As a reminder, the three conventional forms of fall protection are guardrails, safety nets and personal fall arrest systems.

## Slide 222: Additional Fall Protection Systems
In this section we will learn about:
  Handrails and Stair rails
  Floor Hole Covers
  Controlled Access Zones
  Positioning Device Systems
  Alternative Fall Protection
Notes: Additional fall protection systems covered in this section are:
  Handrails and Stair rails
  Floor Hole Covers
  Controlled Access Zones
  Positioning Device Systems
  Alternative Fall Protection

## Slide 223: Handrails and Stairrails - Requirements
Toprail
  36 in. (.9 m) above the tread vertically in line with the riser
  Install handrail 3” from wall
Midrail
  Halfway between toprail and stair stringer
Toe Board
  Minimum of 3 1/2 in. (4 in. nominal) (10.2 cm)
Weight Requirement
  At least 200 lbs. (90.9 kg)
Notes: Explain the requirements for handrails and stairrails.
The toprail must be placed 36 inches above the tread and in-line with the riser, and placed 3 inches from the wall.
The midrail should be halfway between stair stringer and toprail.

## Slide 224: Identify the Hazards
How many hazards do you see in this photo?
Notes: Discuss the hazards you see in this photo. An example of a hazard could be a missing midrail in the top portion of the guardrail. Also, will this system be capable of withstanding 200 pounds of force downward and outward?

## Slide 225: Guardrail boot system
Notes: Describe the properly installed guardrail boot system utilized on the picture on the right.

## Slide 226: Identify the Hazards, continued 1
How many hazards do you see in this photo?
Notes: This photo shows missing handrails on a stairway under construction.

## Slide 227: Hand and Stairrail Solution
Notes: Properly installed metal adjustable guardrail system. Image shows a steel stairrail and hand rail solution installed to a stairway under construction.

## Slide 228: Stair raild installed
Install a toprail 36 in. (.9 m) high to allow one railing to serve as both a handrail and stair rail.
Notes: Properly installed metal adjustable guardrail system. By installing a toprail 36 inches high, allows one railing system to serve as both a hand rail and stairrail.
Discuss how this particular system can be modified to protect workers on stilts by adding a double top rail.

## Slide 229: Starrail Solutions
More Hand and Stairrail Solutions.
Notes: Discuss these two temporary guardrail systems used on a stairway.

## Slide 230: Hole Covers
Secured and marked cover which protects workers from tripping or stepping into or through a hole and keeps objects from falling through a hole
Protects against falls through hazards in this category:
  Floor Holes
Notes: A hole cover is a secured and marked cover which protects workers from tripping or stepping into or through a hole on walking/working surfaces and keeps objects from falling through a hole.

## Slide 231: Hole Covers Are Needed For:
Any hole larger than 2” x 2”, such as:
  Fireplace openings
  Skylights
  Basement stair openings
  Floor heating, ventilating, and air-conditioning (HVAC) registers
  Plumbing floor cutouts
Notes: Hole covers must be used on any hole larger than 2 inches by 2 inches. Examples of these openings include:
Fireplace openings
Skylights
Basement stair openings
Floor heating, ventilating, and air-conditioning (HVAC) registers
Plumbing floor cutouts

## Slide 232: Hole Cover Requirements
Hole Covers must be:
  Capable of supporting at least two times the maximum anticipated load
  Secured from movement by nailing in place or other effective method
  Clearly marked indicating the location of the hole
Notes: Define:
  Window and Wall Openings
  Unprotected Sides and Edges
  Floor Holes

## Slide 233: Hole Covers Must Support 2x Intended Load
Cover floor openings larger than 2” by 2” with material to safely support the working load.
Notes: Discuss whether this floor hole cover is capable of withstanding at least two times the maximum anticipated load?
It is also missing the wording “hole” or “cover” or “hole cover”

## Slide 234: Identify the Hazards, continued 2
How many hazards do you see in this photo?
Notes: Image shows an improper floor hole cover as the cover poses an impalement hazard, does not appear secured to prevent displacement, and is missing the words hole or cover.

## Slide 235: Identify the Hazards, continued 3
How many hazards do you see in these photos?
Notes: These photos show floor hole hazards that are uncovered.

## Slide 236: Identify the Hazards, continued 4
How many hazards do you see in these photos?
Notes: These photos show floor hole hazards that are uncovered and potentially a ladder placed at an improper angle.

## Slide 237: Clearly Marked “Hole” or “Cover”
Notes: This is a picture of a properly installed floor hole cover. This is a Pro-Vent system that can be used to also prevent debris from entering a ventilation system.

## Slide 238: Clearly Marked “Hole” or “Cover”, continued 1
Bright orange paint is a good way to make sure hazards are seen.
Notes: This hole cover is clearly marked and must be properly secured to prevent displacement. It is a best practice to use a bright colored spray paint to be sure that workers know not to remove covers.

## Slide 239: Positioning Device System
A positioning device system is rigged to allow a worker to be supported on an elevated vertical surface, such as a wall, and work with both hands free while leaning.
Notes: A fall positioning device system prevents workers from falling by holding you in-place and preventing you from falling in the first place.

## Slide 240: Positioning Device System, continued 1
Are used to safely position workers away from fall hazards, or in a working position where a fall cannot occur
NOT designed for fall arrest
Must be rigged such that a worker cannot free fall more than 2 feet
Must be secured to an anchor point capable of withstanding 3,000 pounds
Notes: Discuss instances where a positioning system may be used. Examples include encroachment to floor holes or wall openings. This system is designed to prevent workers from ever reaching an area where a fall may occur. Also discuss using shorter lanyards attached directly to the D-ring and the anchor point to securely hold a worker in place to prevent falls from occurring.

## Slide 241: Positioning Device System, continued 2
Inspect for wear, damage, deterioration or defective components prior to EACH USE.
You can wear body belts for positioning device systems not for fall arrest systems.
Best practice is to wear full-body harness even when using positioning device system.
Notes: Similar to a PFAS, a positioning device system must be inspected before each use. You can use a body belt as a positioning device system but not for fall arrest.

## Slide 242: Positioning Device System, continued 3
A body belt or body harness system rigged to allow an employee to be supported on an elevated vertical surface and work with both hands free while leaning.
Notes: Discuss how a positioning device system may be used to stabilize a worker while working at heights.
There are limitations to this system in a residential construction environment.

## Slide 243: Alternative Fall Protection
Residential Construction Exception*
  When employers can demonstrate that it is infeasible or creates a greater hazard to use “conventional” fall protection systems, they must develop and implement a fall protection plan, as needed, in accordance with §1926.502(k).
Notes: Discuss how a positioning device system may be used to stabilize a worker while working at heights.
There are limitations to this system in a residential construction environment.

## Slide 244: What does “Infeasible” mean?
Source: 1926.500(b)
Infeasible means:
  Impossible to perform construction work using conventional fall protection or
  It is technologically impossible to use conventional fall protection
Notes: These examples are found directly in OSHA’s Preamble to the 1994 Subpart M-Fall Protection rulemaking record.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 245: Examples of Infeasibility
Source: Preamble to Final Fall Protection Rule, Section 3 - III. Summary and Explanation of the Final Rule, August 9, 1994
OSHA believes it would be unreasonable to expect a home builder to rent a crane when the jobsite is difficult to access (terrain or remote location) or when the home builder has only a single roof to raise.
OSHA does not expect home builders to erect scaffolds around the entire perimeter of a house, or to take other extremely burdensome measures such as erecting separate structures (telephone poles, e.g.) and stringing a lifeline to use as an attachment point for personal fall arrest equipment.
Notes: OSHA does not consider "economic infeasibility" to be a basis for failing to provide conventional fall protection for employees performing residential construction work.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 246: What does “Creating a Greater Hazard” mean?
Source: Preamble to Final Fall Protection Rule, Section 3 - III. Summary and Explanation of the Final Rule, August 9, 1994
Hazards created by compliance with the standard are greater than those created by non-compliance.
Notes: If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 247: Establishing “Greater Hazard”, cont.
Source: Preamble to Final Fall Protection Rule, Section 3 - III. Summary and Explanation of the Final Rule, August 9, 1994
OSHA acknowledges that, regardless of an employer's ability to preplan for fall protection, there may be cases where the installation or use of conventional fall protection systems poses a greater hazard than that to which employees performing the construction work would otherwise be exposed.
OSHA expects an employer who seeks to make that case to indicate specifically how compliance with the requirement for conventional fall protection systems would pose a greater hazard.
OSHA will assess each such case on its particular merits.
Notes: Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 248: Fall Protection Plan
This option is available for those engaged in “residential construction” work who can establish that conventional fall protection is infeasible or creates a greater hazard.
Note: It is OSHA’s presumption that conventional fall protection is feasible and will not create a greater hazard, and it is the employer’s burden to establish that it is appropriate to implement a fall protection plan.
Notes: Discuss: Employers cannot use alternative fall protective measures until it has been documented and proven that conventional fall protective systems are either infeasible/their use creates a greater hazard.
This includes OSHA’s Appendix E to Subpart M, employers must exhaust all conventional means of providing fall protection prior to implementing a fall protection plan that meets the requirements of 1926.502(k).

## Slide 249: Fall Protection Plan, continued 1
A qualified person develops the plan.
A competent person implements the plan.
Site-specific and written plan that identifies and evaluates fall hazards on a jobsite, establishes the protection methods to be used, and assesses the ability of workers to follow related work rules and use equipment safely.
Notes: Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 250: Fall Protection Plan, continued 2
Source: Preamble to Final Fall Protection Rule, Section 3 - III. Summary and Explanation of the Final Rule, August 9, 1994
OSHA considers the implementation of a fall protection plan, outlining alternative fall protection measures, to be a “last resort”!
  Allowed only where the other options for fall protection have been exhausted.
Notes: Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 251: Fall Protection Plan, continued 3
A fall protection plan must identify how and where fall protection will be used on the jobsite and also the safe work practices that will be used.
NOTE: Prior to implementing a fall protection plan (1926.502(k)) the employer has the burden to establish why the use of conventional fall protection is infeasible or creates a greater hazard
Notes: A written fall protection plan identifies and evaluates fall hazards on a jobsite, establishes the protection methods to be used, and assesses the ability of workers to follow related work rules and use equipment safely.
The plan identifies protective methods for hazards in this category: Leading Edges

## Slide 252: Fall Protection Plan, continued 4
Documents reasons why the use of conventional fall protection systems are infeasible or their use creates a greater hazard.
Includes a written discussion of other measures that will be taken to reduce or eliminate the fall hazard.
Identifies locations where conventional fall protection cannot be used and then classify these areas as controlled access zones (CAZ).
Notes: Discuss what is required in a fall protection plan, and refer back to the definition of “qualified person” and “competent person” (if needed).
Note: the employer has the burden to establish that conventional fall protective systems are either infeasible or their use creates a greater hazard.

## Slide 253: Fall Protection Plan, continued 5
Must be written and site specific
A written plan developed for the repetitive use for a particular style/model home would be considered site-specific with respect to a particular site only if it fully addresses all issues related to fall protection at that site
Notes: Previously under OSHA’s Interim Fall Protection Compliance Guidelines for Residential Construction, employers had the option to utilize a fall protection plan without prior showing of infeasibility/greater hazard and without having a written site-specific fall protection plan.
Beginning June 16, 2011 employers engaged in residential construction that establish that conventional fall protection systems are either infeasible or create a greater hazard and implement a fall protection plan meeting the requirements of 1926.502(k) will be required to establish a written and site-specific fall protection plan.

## Slide 254: Fall Protection Plan, continued 6
Write it down & keep at jobsite
Must be kept current and up-to-date
Implementation/supervision by designated individuals
Must include:
  Reasons “conventional” fall protection are infeasible or create greater hazard
  Alternative measures to reduce or eliminate fall hazards
  Location and who can work in Controlled Access Zone (CAZ)
Notes: Discuss the requirements of a fall protection plan.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.

## Slide 255: Establishing a Controlled Access Zone (CAZ)
Designated/restricted work area that may have increased hazards related to otherwise unprotected fall hazards and/or falling material.
Restricts access to processes found in this hazard category:
  Leading Edges
Notes: A controlled access zone is a designated/restricted work area that may have increased hazards related to otherwise unprotected fall hazards and/or falling material.

## Slide 256: Requirements for a CAZ
The competent person must:
Determine where to place the boundaries of a CAZ.
Ensure that the requirements of the fall protection plan are in place before work begins in a CAZ.
Monitor workers while they are in a CAZ; correct any unsafe practices or conditions immediately.
Notes: In a CAZ, a competent person must determine where to place the boundaries, ensure that the requirements of the fall protection plan are in place and monitor workers while they are in a CAZ. They must also correct any unsafe practices or conditions immediately.

## Slide 257: Requirements for a CAZ, continued 1
The controlled access zone must be:
Posted at the perimeter in plain view.
Clearly visible to a person approaching the area.
Restricted to authorized personnel.
Notes: In a CAZ, the area must be posted at the perimeter, clearly visible to anyone approaching the area and restricted to unauthorized personnel.

## Slide 258: Evaluation Section
The following section is meant to provide an open forum for discussion between attendees and instructors.
Note: The practices and procedures shown may or may not meet the intent of OSHA’s Subpart M-Fall Protection requirements, check with your Local OSHA Area Office prior to implementing alternative fall protection procedures.
Notes: Instructor: Please review this slide with student attendees.
The following slides are meant to start discussions regarding when it may be appropriate to implement alternative fall protection procedures and a written fall protection plan.
This section is intended to assist employers in their efforts to comply with fall protection requirements for residential construction work. The Occupational Safety and Health Act requires employers to comply with safety and health standards promulgated by OSHA or by a state with an OSHA-approved state plan.
The burden is on each employer to determine when it may be appropriate to use alternative fall protection procedures, and should check with their Local Area OSHA Offices prior to implementing these procedures on a jobsite.

## Slide 259: Discuss Fall Hazards
Discuss: Is conventional fall protection required?
Notes: Engage the audience and facilitate a discussion on this picture.
The worker is exposed to an interior fall hazard of 6 feet or more, however one might argue that is infeasible or creates a greater hazard to use a conventional fall protection system.
What type of conventional fall protection methods can be used to protect this worker from an interior fall hazard?
Explain the safe work practices that should be utilized to safety protect workers who are performing these tasks, which should include the use of conventional fall protection systems (personal fall arrest systems, guardrails, or safety nets) and ladders and scaffolding.
This picture shows the installation of floor joists and the worker is working from the ground to set them into place; however they are exposed to an interior fall hazard of 6 feet or more.
Discuss the installation of the floor joist, and the process to do so.
Limitations of conventional fall protection systems during the installation of floor joists may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Manufacturers of the floor joists may prohibit inserting anchor points that may cause the joist to crack or fail.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: It is important to remember that employers must demonstrate why conventional fall protection is either infeasible or creates a greater hazard for each part of a task prior to implementing alternative fall protection measures and a written fall protection plan. There are numerous parts of each job task that goes into the construction of a house, and throughout the duration of a specific task there may be a combination of conventional and alternative safe work practices that may be utilized. In order to remain in compliance with OSHA’s Subpart M- Fall Protection regulation employers have the burden of establishing a written argument as to why alternative fall protection procedures were used and where conventional fall protection systems were either infeasible or created a greater hazard.

## Slide 260: Discuss Fall Hazards
Discuss: Is conventional fall protection required?, continued 1.
Notes: Engage the audience and facilitate a discussion on this picture.
The worker is exposed to an interior fall hazard of 6 feet or more, however one might argue that is infeasible or creates a greater hazard to use a conventional fall protection system.
What type of conventional fall protection methods can be used to protect this worker from an interior fall hazard?
Explain the safe work practices that should be utilized to safety protect workers who are performing these tasks, which should include the use of conventional fall protection systems (personal fall arrest systems, guardrails, or safety nets) and ladders and scaffolding.
This picture shows the installation of floor joists and the worker is working from the ground to set them into place; however they are exposed to an interior fall hazard of 6 feet or more.
Discuss the installation of the floor joist, and the process to do so.
Limitations of conventional fall protection systems during the installation of floor joists may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Manufacturers of the floor joists may prohibit inserting anchor points that may cause the joist to crack or fail.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: It is important to remember that employers must demonstrate why conventional fall protection is either infeasible or creates a greater hazard for each part of a task prior to implementing alternative fall protection measures and a written fall protection plan. There are numerous parts of each job task that goes into the construction of a house, and throughout the duration of a specific task there may be a combination of conventional and alternative safe work practices that may be utilized. In order to remain in compliance with OSHA’s Subpart M- Fall Protection regulation employers have the burden of establishing a written argument as to why alternative fall protection procedures were used and where conventional fall protection systems were either infeasible or created a greater hazard.

## Slide 261: Discuss Fall Hazards
Discuss: Is this the correct application for conventional fall protection?
Notes: This picture shows three workers attached to separate self-retracting lifelines (SRL) to protect from fall hazards of 6 feet or more.
Discuss the installation of floor sheathing.
Limitations of conventional fall protection systems during the installation of floor sheathing may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Manufacturers of the floor joists may prohibit inserting anchor points that may cause the joist to crack or fail.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: It is important to remember that employers must demonstrate why conventional fall protection is either infeasible or creates a greater hazard for each part of a task prior to implementing alternative fall protection measures and a written fall protection plan. There are numerous parts of each job task that goes into the construction of a house, and throughout the duration of a specific task there may be a combination of conventional and alternative safe work practices that may be utilized. In order to remain in compliance with OSHA’s Subpart M- Fall Protection regulation employers have the burden of establishing a written argument as to why alternative fall protection procedures were used and where conventional fall protection systems were either infeasible or created a greater hazard.

## Slide 262: Discuss Fall Hazards
This picture shows the use of both conventional and alternative fall protection procedures, which still requires the use of a written, site-specific fall protection plan
Notes: Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
This picture shows the installation of the second row of sheathing, and utilizes both guardrails to protect from an exterior fall and the use of alternative safe work practices that show workers working from a previously established deck.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of floor sheathing may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Manufacturers of the floor joists may prohibit inserting anchor points that may cause the joist to crack or fail.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 263: Discuss Fall Hazards
6 Feet
Employers must first exhaust all options to provide conventional fall protection, or other work methods covered by OSHA regulations prior to implementing a safety monitor system and warning line
Discuss: Can conventional fall protection be provided?
Notes: Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
This picture shows the installed deck of floor sheathing in preparation for the installation of exterior walls. There is a warning line painted that is part of a safety monitor system. This shows an example of an alternative fall protection procedure.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of exterior walls may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Manufacturers of the floor joists may prohibit inserting anchor points that may cause the joist to crack or fail.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 264: Discuss Fall Hazards
Discuss: Can conventional fall protection be provided?, continued 1
Notes: Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
This picture shows the installed deck of floor sheathing in preparation for the installation of exterior walls. Workers are in the process of erecting the 2nd floor exterior walls.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of exterior walls may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 265: Discuss Fall Hazards
This picture shows the use of guardrails to protect against exterior fall hazards
Notes: This picture shows the installation of floor sheathing, and utilizes guardrails to protect from an exterior fall hazard. It is unclear what type of conventional or alternative fall protection is provided to the workers on the floor deck.
Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of floor sheathing may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Manufacturers of the floor joists may prohibit inserting anchor points that may cause the joist to crack or fail.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 266: Discuss Fall Hazards
Discuss: Can conventional fall protection be provided?, continued 2
This picture shows the use of both conventional and alternative fall protection procedures, which still requires the use of a written, site-specific fall protection plan
Notes: This picture shows the use of both conventional and alternative fall protection procedures utilized to set and brace roof trusses. Employers must determine and evaluate each job task to determine when and where conventional fall protection can be provided, prior to implementing alternative fall protection procedures.
Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of roof trusses may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Roof trusses are not designed to resist lateral impact loads.
A falling worker attached to a single roof truss could cause all the trusses to collapse.
Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Manufacturers of the roof trusses may prohibit inserting anchor points that may cause the truss to fail.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 267: Discuss Fall Hazards
Employers must first exhaust all options to provide conventional fall protection, or other work methods covered by OSHA regulations prior to implementing alternative fall protection procedures
Discuss: Can conventional fall protection be provided?, continued 3
Notes: Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of floor joists may include:
Roof trusses are not designed to resist lateral impact loads.
A falling worker attached to a single roof truss could cause all the trusses to collapse
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Manufacturers of the roof trusses may prohibit inserting anchor points that may cause the truss to fail.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 268: Discuss Fall Hazards
Discuss: Can conventional fall protection be provided?, continued 4
Notes: This picture shows the use of both ladders and alternative fall protection procedures utilized to set and brace roof rafter portions. Employers must determine and evaluate each job task to determine when and where conventional fall protection can be provided, prior to implementing alternative fall protection procedures.
Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of roof rafters and while stick framing may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Roof rafters are not designed to resist lateral impact loads.
Roof structures are unstable until some sheathing is installed.
A falling worker attached to a single rafter could cause the entire roof portion to fail.
Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Manufacturers of the roof trusses may prohibit inserting anchor points that may cause the truss to fail.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 269: Discuss Fall Hazards
This picture shows the use of conventional fall protection procedures, notice the personal fall arrest systems.
Notes: This picture shows the use of a personal fall arrest system utilized to set and brace roof rafter portions. Employers must determine and evaluate each job task to determine when and where conventional fall protection can be provided, prior to implementing alternative fall protection procedures.
Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of roof rafters and while stick framing may include:
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Roof rafters are not designed to resist lateral impact loads.
Roof structures are unstable until some sheathing is installed.
A falling worker attached to a single rafter could cause the entire roof portion to fail.
Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Manufacturers of the roof trusses may prohibit inserting anchor points that may cause the truss to fail.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 270: Discuss Fall Hazards
Employers must first exhaust all options to provide conventional fall protection, or other work methods covered by OSHA regulations prior to implementing alternative fall protection procedures
Discuss: Can conventional fall protection be provided?, continued 5
Notes: Install slide guards on steep pitched roofs after the first row of sheathing is installed.
OSHA’s new compliance directive has not outlawed the use of slide guards or safety monitors.
  Now, employers must first demonstrate that it is infeasible to comply with the provisions of the standard, or that it creates a greater hazard.
  Then they can use those systems as part of a written, site-specific fall protection plan that meets the requirements of 1926.502(k).
Slide guards cannot simply be used in lieu of conventional fall protection methods under 1926.501(b)(13). However, slide guards may be used as part of a written, site-specific fall protection plan that meets the requirements of 1926.502(k) if the employer can demonstrate that the use of conventional fall protection (i.e., guardrail, safety net, or personal fall arrest systems) would be infeasible or create greater hazards.
Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of roof sheathing may include:
Roof trusses are not designed to resist lateral impact loads.
Roof structures are unstable until some or all sheathing is installed
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Installation of guardrail system could involve more risk, due to the duration of the fall exposure.
Manufacturers of the roof trusses may prohibit inserting anchor points that may cause the truss to fail.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 271: Discuss Fall Hazards
Discuss: Can conventional fall protection be provided?, continued 6
Notes: Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
This picture shows an installed working platform in the attic, which is an example of an alternative fall protection procedure.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems while performing attic work may include:
Even if an anchor point is used, the use of a personal fall arrest system through rafters and trusses creates an added swing fall hazard.
Installation of anchor point exposes a worker to a fall hazard when they are unprotected while installing the anchor point in the peak of the attic.
A falling worker attached to a single roof truss could cause all the trusses to collapse.
Lack of a suitable anchor point to withstand 5000 pounds or twice the intended load from a falling worker.
Manufacturers of the roof trusses may prohibit inserting anchor points that may cause the truss to fail.
Manufacturers of personal fall arrest system components may prohibit the anchor point to be placed at ground level, or below a workers ‘D’ ring on their harness.
Clearance distance below a worker, which is needed when using a personal fall arrest system, may not be sufficient to prevent the worker from contacting the next lower level, should a fall occur.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 272: Discuss Fall Hazards
Discuss: Can conventional fall protection be provided?, continued 7
Notes: This picture shows the installation of an anchor point prior to performing roofing work.
Employers must determine and evaluate each job task to determine when and where conventional fall protection can be provided, prior to implementing alternative fall protection procedures.
Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Discuss: How can you provide conventional fall protection for this worker who is installing anchor points?
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 273: Discuss Fall Hazards
Discuss: Can conventional fall protection be provided?, continued 8
Notes: This picture shows installation of permanent stair rails. Employers must determine and evaluate each job task to determine when and where conventional fall protection can be provided, prior to implementing alternative fall protection procedures.
Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the installation of permanent stair rails may include:
Hand rail is custom built on the jobsite, which requires the carpenter to measure and cut frequently. This also requires the installer to go up and down the stairs to measure, cut and level the rail components. The use of a personal fall arrest system would require the carpenter to attach to an anchor point at 6 feet and then detach hundreds of times, in addition to an added slip, trip and fall hazard introduced into a small working surface, i.e. stairway.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 274: Discuss Fall Hazards
Discuss: Can conventional fall protection be provided?, continued 9
Notes: This picture shows the construction of decks attached to a home. Employers must determine and evaluate each job task to determine when and where conventional fall protection can be provided, prior to implementing alternative fall protection procedures.
Discuss: Employers must evaluate the use of conventional fall protection systems, and other work practices covered under OSHA standards (i.e. ladders, scaffolding or aerial lifts) prior to implementing any alternative work practices and establishing a written, site-specific fall protection program.
If an employer can demonstrate that conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) is infeasible or presents a greater hazard, a written, site specific fall protection plan meeting the requirements of 1926.502(k) can be implemented.
The employer has the burden of establishing that it is appropriate to implement a fall protection plan.
Limitations of conventional fall protection systems during the construction of decks attached to the home may include:
Clearance distance below a worker, which is needed when using a personal fall arrest system , may not be suitable to prevent the worker from contacting the next lower level, should a fall occur.
The use of guardrails would prevent the carpenter from installing permanent portions of the deck.
Manufacturers may have differing installation/usage requirements; always refer to the manufacturers’ instruction prior to use.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement one of the conventional fall protection methods (personal fall arrest system, guardrails, or safety nets); and accordingly the employer has the burden of establishing that it is appropriate to implement a fall protection plan that complies with 1926.502(k).

## Slide 275: Section 6
Fall Protection Rescue plan

## Slide 276: Disclaimer
This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.
This presentation is intended to discuss Federal Regulations only - your individual State requirements may be more stringent as many states operate their own state OSHA and they may have adopted construction standards that are different from information presented in this training. If you live in a state with an OSHA approved state plan, you should contact your local administrator for further information on the standards applicable in your state.
These materials are meant for informational purposes only.
No representation is made as to the thoroughness of the presentation.
Notes: This material was produced under grant number SH-31198-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05122-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 277: Disclaimer, continued 1
It is not the intent to provide compliance-based training in this presentation, the intent is more to address hazard awareness in the residential construction (i.e. home building) industry, and to recognize the overlapping hazards present in many construction workplaces.
Photos shown in this presentation may depict situations that are not in compliance with applicable OSHA/safety requirements.
No legal advice is offered or implied, and no attorney-client relationship is intended or established. If legal advice or other expert assistance is required the services of a competent professional person should be sought.
It is the responsibility of the employer and its employees to comply with all pertinent OSHA/safety rules and regulations in the jurisdiction in which they work.
Notes: Please read the disclaimer for legal purposes, this is required under the Susan Harwood Training Grant program.

## Slide 278: Copyright Information © 2018
This material is the copyrighted property of the Job-Site Safety Institute and the National Association of Home Builders. By federal regulation, OSHA reserves a license to use and disseminate such material for the purpose of promoting safety and health in the workplace. The Job-Site Safety Institute and the National Association of Home Builders hereby authorizes employers and workplace safety and health professionals to use this material, distributed by or through OSHA, in their workplaces or practices in accordance with the guidance contained in the material.
To this end, permission is granted to use such copyrighted material solely for non-commercial, instructional, personal, or scholarly purposes. The material may be used and incorporated into other workplace safety and health programs on the condition that no fee may be charged for the subsequent use of the material. Use of the material for any other purpose, particularly commercial use, without the prior, express written permission of the copyright owner/s is prohibited. Furthermore, any modification to the material is prohibited without the prior, express written permission of the copyright owners.
Notes: Note that the these materials are copyrighted by the Job-Site Safety Institute and the National Association of Home Builders. Permission is granted to use such copyrighted material in accordance with the terms on the slide.

## Slide 279: Learning Objectives: Section 6
Learn the importance of implementing a plan to rescue workers who experience a fall.
Learn about the hazards of not quickly rescuing a suspended worker.
Discuss sample procedures in a fall protection rescue plan.
Notes: Discuss the learning objectives for Section 6. In this section, attendees will learn the importance of implementing a plan to rescue workers who experience a fall, the hazards of not quickly rescuing a suspended worker and sample procedures in a fall protection rescue plan.

## Slide 280: Fall Protection Rescue Plan
Describes the steps taken to rescue a fallen worker, even if they are wearing a PFAS.
Sample Procedures Include:
  Ensuring the plan can safely rescue a suspended worker within 3-4 minutes of falling.
  Contacting appropriate emergency personnel.
  Using ladders or other methods to rescue worker.
Notes: A fall protection rescue plan describes the steps taken to rescue a fallen worker, even if they are wearing a PFAS.

## Slide 281: Fall Protection Rescue Plan, continued 1
Most rescues fail because there is no thought to how we would rescue a worker in the event of a fall.
Think whether you have the proper equipment on-site to rescue a fallen worker.
Notes: Most rescues fail because they are not preplanned. Think about whether you have the right equipment to rescue a worker in the event they experience a fall.

## Slide 282: Fall Protection Rescue Plan, continued 2
Are your employees trained in basic first-aid?
Are there adequate first-aid supplies available?
Is there a hospital or urgent care facility nearby?
  Do you know where it is located?
  Is the address and phone number of nearest emergency care center posted and do employees know where this is located?
Notes: Most rescues fail because they are not preplanned. Think about whether you have the proper training to administer basic first-aid or CPR in the event a worker experiences a fall.

## Slide 283: Fall Protection Rescue Plan, continued 3
Suspended workers are at risk of suspension trauma.
Prolonged suspension from fall arrest systems can cause orthostatic intolerance, which, in turn, can result in serious physical injury, or potentially, death.
Rescue workers within minutes to prevent pooling of blood in lower extremities/orthostatic intolerance.
Notes: Prolonged suspension from fall arrest can cause orthostatic intolerance, which can lead to death within 30 minutes or sooner.

## Slide 284: Fall Protection Rescue Plan, continued 4
Research indicates that suspension in a fall arrest device can result in unconsciousness, followed by death, in less than 30 minutes.
Rescue suspended workers as quickly as possible.
Be aware of signs and symptoms of orthostatic intolerance.
Suspended workers with head injuries or who are unconscious are particularly at risk.
Be aware of factors that can increase the risk of suspension trauma.
Notes: Discuss the hazards of not rescuing a worker quickly. Be aware of signs and symptoms of orthostatic intolerance. Suspended workers with head injuries or who are unconscious are particularly at risk.

## Slide 285: Rescue Planning
Examples of rescue equipment:
  Ladder Rescue
  Pole
  Rescue Rope
  Scaffold
  Crane
  Aerial Lift
  Alternative Lifting & Lowering Device
Notes: Discuss examples of rescue equipment, which include ladders, pole, rescue rope, scaffold, crane, aerial lift or alternative lifting and lowering devices.

## Slide 286: Rescue Training
Employees should be trained to:
Understand and be able to evaluate the risks associated with working at heights.
Must be trained and competent in the use of fall protection equipment prior to conducting work at heights.
To report unsafe conditions or behaviors.
To be familiar with and understand the company’s rescue plan to provide prompt rescue in the event of an arrested fall event.
Notes: Discuss the areas that workers should be trained and familiar in order to be comfortable with responding to a worker who experienced a fall. Workers should understand and be able to evaluate the risks associated with working at heights, on the use of fall protection equipment prior to conducting work at heights, to report unsafe conditions or behaviors and be familiar with and understand the company’s rescue plan to provide prompt rescue in the event of an arrested fall event.

## Slide 287: Plan for Self-Rescue
If the proper fall protection is used, 90% of workers will be able to perform a Self-Rescue, which should include these steps:
  1. Climbing back up to the level from which he fell (from a few inches to 2-3 feet).
  2. Returning to the floor or ground to be evaluated for possible medical attention per OSHA.
  3. Removing all components of fall arrest system impacted by the fall event from service and documenting (bag and tag) the components with name, date and activity at time of fall and giving the equipment to management.
Notes: If proper fall protection is used, 90% of workers can be capable of performing a self-rescue. There are three steps to follow in the event of a self-rescue:
  1. Climbing back up to the level from which he fell (from a few inches to 2-3 feet).
  2. Returning to the floor or ground to be evaluated for possible medical attention per OSHA.
  3. Removing all components of fall arrest system impacted by the fall event from service and documenting (bag and tag) the components with name, date and activity at time of fall and giving the equipment to management.

## Slide 288: Examples of Self-Rescue Devices
Self-rescue ladder attachment. This can be added to your harness as part of a PFAS.
Notes: Discuss the use of a self-rescue ladder attachment that can be added as part of a PFAS to allow for self-rescue in the event of a fall.

## Slide 289: Examples of Self-Rescue Devices, continued 1
Self-Rescue system is a harness mounted backpack containing a controlled descent device.
In event of a fall, the user pulls a shoulder strap mounted release cord lowering the fallen worker safely to the ground.
Notes: Discuss the use of a Controlled Descent Device that can be added as part of a PFAS to allow for self-rescue in the event of a fall. Photo: DBI/SALA Self-Rescue 50 Controlled Descent Device.

## Slide 290: Examples of Rescue Devices
A rescue pole allows a coworker to attach to your d-ring and safely lower you to the ground.
Notes: Discuss the use of a rescue pole that can be used to allow an assisted rescue in the event of a fall.

## Slide 291: What goes in your Written Rescue Plan?
Types of rescue equipment available to workers.
Locations of any rescue line anchor points for rope rescue.
How to attach retrieval or lowering lines to a fallen workers’ harness.
Specifics about training required to perform rescue work.
Other site-specific details needed for a safe and successful rescue.
Name and physical location of jobsite and contact information of competent person or company officials.
Notes: Discuss elements of a written fall rescue plan.

## Slide 292: Have questions? Need More Information?
Call NAHB’s toll-free phone “Technical Assistance Hotline” at: 1-800-368-5242.
Send an email to: safety@nahb.org
Visit: nahb.org/safety | jssafety.org

## Slide 293: Thanks for Participating!
Post test Next……